## Slide 1: The curse of abundance – An attempt to design a hydrological multimodel system for forecasting purposes over Europe
Fredrik Wetterhall
Emanuel Dutra, Chantal Donnelly, Lena Strömbäck, Peter Salamon, Lorenzo Alfieri, Konrad Bogner, Florian Pappenberger, Blazej Kreminski, Gianpaolo Balsamo

## Slide 2: The European Flood Awareness System: what is it?
Multiple weather forecasts (and other data)
Hydrological model
Flood forecast and warnings
Added value: Early warning system for river floods, complementary to MS systems
Providing National Flood Forecasting Agencies and Emergency Response Coordination Centre (ERCC) with probabilities of flooding 3-15 days in advance for all Europe (typically 4-6 days)
EFAS provides early warning information only; informing the public and civil protection is done by the national forecasting centers and ERCC (ERCC daily to National Civil Protection)
EFAS went fully operational October 2012
40 member organisations
R194

## Slide 3: What do users want from EFAS?
At the EFAS annual meeting 2012 we asked >30 operational forecasters about what they most wanted improved in EFAS (Wetterhall et al., 2013, HESS), and the top priorities were:
“Introduce multi-model approach for meteorology AND hydrology”
Advantage: Full assessment of model uncertainty and a more robust system (more trust)
Disadvantage: More uncertainty,
not straight-forward in decision making
Longer run times
R197

## Slide 4: Forecasting chain in EFAS
EPS
Hydrology
Warning
Preprocessing/
calibration
Postprocessing
Verification
Feedback to the model

## Slide 5: Forecasting chain in future EFAS
EPS
Hydrology
Warning
Preprocessing/
calibration
Postprocessing
Verification
Feedback to the model
Hydraulics
Multimodel
R212

## Slide 6: Criteria for the hydrological models to be included
open source code
existing user community
flexibility to grid structure, sub-basin and basin scale requirements with a possibility to be coupled to different land-surface schemes (e.g. HTESSEL, CLM, SWAT, etc.)
possibility of calibration with suitable tools
flexibility in grid resolution between 1km and 10 km
facility of introducing discharge observation stations for comparison and calibration purposes.
pan European model set up already existing or, in case not existent, feasibility to set up European model
CLM | mHM
E-HYPE | MPI-HM
G2G | NOAH-MP
GWAVA | ORCHIDEE
H08 | PCR-GLOBWB
HTESSEL | SWAT
JULES | SWIM
LaD | TOPLATS
LISFLOOD | VIC
LPJml | WASMOD-M
Mac-PDM | WaterGAP
MATSIRO | WBMplus

## Slide 7: Initial test of three models
Hydrological models | LISFLOOD | HTESSEL/ CAMA | EHYPE
Characteristic | Hydrological model with channel routing | HTESSEL coupled with CamaFlood | Semi-distributed conceptual model
Resolution | 5 km gridded | 80 km land surface model 25 km routing | Catchment based (varying resolution)
Driving data | 5 km gridded observed data | ERA-Interim corrected with GPCP/ 5 km gridded observed data | ERA-Interim corrected with GPCC/ 5 km gridded observed data
Test period: 1990-2010
Observational discharge: 212 stations from GRDC

## Slide 8: LISFLOOD
Notes:   Raster-based model developed at JRC
  Input maps of precipitation, temperature and evapotranspiration
  Output maps of surface runoff, rapid and slow groundwater
  Channel routing through kinematic wave
  Currently setup over Europe on a 5 x 5 grid for EFAS

## Slide 9: HTESSEL and CaMa-Flood
Notes: HTESSEL:
  ECMWF land surface scheme with new soil (Balsamo 2009 JH) and snow hydrology (Dutra 2010 JH)
  Surface and soil runoff
  4-layers in soil, no active groundwater component
  Coupled with operational ECMWF models but also as a stand-alone offline model
CaMa-Flood: Catchment-based Macro-scale Floodplain model (Yamazaki, 2011 WRR).
  Distributed river routing model
  River and floodplain storage with sub-grid topographic parameters
  Diffusive wave equation along river network map.
  Input: Fine-resolution (1 km) datasets SRTM30 DEM & GDBD Flow Direction Map

## Slide 10: E-HYPE – pan European HYPE application
Notes:   Semi-distributed
  35000 subbasins
  Median size 215 km2
  Set-up using continental (and global) databases
  Input: Precipitation and temperature subbasin averages

## Slide 11: Results: Nash-Sutcliffe and mean relative error

## Slide 12: Catchment area

## Slide 13: Rhein 160800 km2
Observed NS MRE
LISFLOOD 0.89 9.4
HTESSEL 0.25 -9.6
EHYPE 0.65 -7.6

## Slide 14: Danube 658400 km2
Observed NS MRE
LISFLOOD 0.55 6.2
HTESSEL 0.62 -12
EHYPE 0.32 -14

## Slide 15: Severn 4000 km2
Observed NS MRE
LISFLOOD 0.64 21
HTESSEL 0.45 17
EHYPE 0.81 6.4

## Slide 16: Multimodel – how useful is it for decision making?

## Slide 17: Create one supermodel to rule them all?
Bayesian Model Averaging (BMA) accounts for the model uncertainty by averaging over the best models according to posterior model probability
The BMA methodology applied for this study performs analysis assuming a uniform distribution on model priors and using a simple BIC (Bayesian Information Criterion) approximation to construct the prior probabilities on the regressions coefﬁcients (Raftery, Hoeting, Volinsky, Painter & Yeung 2010).
If M = {,…, } denotes the set of models and if is the quantity of interest (e.g. stream-flow), then the posterior distribution of given the data D is:
This is an average of the posterior distributions under each model weighted by the corresponding posterior model probabilities.

## Slide 18: Results: Bayesian model averaging
BMA improves NSE in 76% of the cases

## Slide 19: Results: Bayesian model averaging
 | BMA | LISFLOOD | HTESSEL | E-HYPE
Best model before |  | 84 % | 3% | 13 %
Best model after | 76% | 24% | - | -
NS median | 0.76 | 0.66 | 0.087 | 0.36

## Slide 20: Very preliminary conclusions
There are many models potentially suitable for inclusion in EFAS
The different models do perform differently depending on basin characteristics
BMA improves the performance of the models in most cases, and gives reasonable results even if the individual models are not doing well in a particular catchment
Without proper calibration it is difficult to draw conclusions on the quality of the driving data
Combining models will be a challenge – ensemble of models or weighted mean?
Is it necessary? Largest bias and uncertainty still in the NWP!
Future steps
Further calibration of LISFLOOD and CaMaFlood
Performance of the models probabilistic operational mode
Forecast display and dissemination
R201

## Slide 21: Thank you for your attention!

## Slide 22: Results: Correlation LISFLOOD, HTESSEL/Cama and EHYPE

## Slide 23: Influence of the observed precip data used on the results
Corrected ERAI and EFAS 5km gridded datasets perform on par.
The height correction is too wet
The EFAS 5km gridded has the best water balance
OBS! E-HYPE in this version is only rudimentary calibrated

## Slide 24: Pite River (northern Sweden)
Observed NS MRE
LISFLOOD 0.55 6.2
HTESSEL 0.62 -12
EHYPE 0.32 -14