## Slide 1
Inter-system biases estimation in multi-GNSS relative positioning with GPS and Galileo
Cecile Deprez and Rene Warnant
University of Liege, Belgium

## Slide 2: Multi-GNSS
Many systems : GPS, GLONASS, Galileo, BeiDou, QZSS, IRNSS
  Possibility for Multi-GNSS RTK !
  Independent but compatible…
  Improved reliability – availability - precision

## Slide 3: Multi-GNSS
Overlapping frequencies :
    L1 (GPS) – E1 (Galileo) – B1 (BeiDou) – L1 (QZSS)
    L5 (GPS) – E5a (Galileo) – L5 (QZSS) – L5 (IRNSS)
    L2 (GPS) – L2 (QZSS)
    E5b (Galileo) – B2 (BeiDou)
GLONASS
GPS
BeiDou
Galileo
E5a
L5
E5b
E6
L2
L2
B2
B3
Lower L-Band
L5
E1
L1
L1
B1
Upper L-Band
1176,45
1191,795
1207,14
1227,60
1247,00
1268,52
1278,75
1575,42
1602,00
Frequency (Mhz)

## Slide 4: Inter-system Biases (ISBs)
One-way code observable model
  GPS :
  Galileo :
: Pseudo-range : Receiver clock errors
: Geometric distance : Satellite clock errors
: Tropospheric delay : Receiver hardware delay
: Ionospheric delay : Satellite hardware delay
: Multipath : Code noise
Galileo to GPS
Time Offset
=
Different Time Systems

## Slide 5: Inter-system Biases (ISBs)
In a ZERO baseline case :
  Single Difference
  Double Difference
The GGTO term disappears
4 unknowns :
X,
Y,
Z,
Differential hardware delay between GPS and Galileo (ISB)
Single reference satellite for all observations

## Slide 6: Equipment
Receivers :
  2 x Septentrio PolaRx4 (Sept 1 & Sept 2)
  2 x Trimble NetR9 (TRM 1 & TRM 2)
  1 x Septentrio PolaRxS (Sept 3)
Antennae :
  2 x TRIMBLE TRM 59800 SCIS (choke ring antenna) (ULG0 & ULG1)
Splitter :
  1 x 2-way splitter
  1 x 4-way splitter
Fixed precise coordinates

## Slide 7: Configurations
End of 2014 – DOY 179 of 2015
ULG0
TRM1
TRM2
ULG1
Sept1
Sept3
ULG0
TRM1
Sept1
ULG1
TRM2
Sept3
ULG0
TRM1
TRM2
ULG1
Sept1
Sept2
ULG0
TRM1
Sept2
ULG1
Sept1
Sept3
TRM2
DOYs180-292 of 2015
DOYs 293-365 of 2015 – DOYs 1-12 of 2016
DOYs 13 –now of 2016

## Slide 8: Results
 |  | GPS L1/Galileo E1 |  |  |  | GPS L5/Galileo E5a |  |  | 
 |  | Mean ISB (m) |  | Std ISB (m) |  | Mean ISB (m) |  | Std ISB (m) | 
 |  | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min
Sept2 – Sept1 | 14’ | NO DATA |  |  |  |  |  |  | 
 | 15’ | 0,004 | 0,003 | 0,003 | 0,003 | 0,005 | 0,008 | 0,004 | 0,008
 | 16’ | 0,002 | 0,002 | 0,000 | 0,001 | 0,002 | 0,008 | 0,003 | 0,008
Sept2 – Sept3 | 14’ | NO DATA |  |  |  |  |  |  | 
 | 15’ | 0,001 | 0,001 | 0,004 | 0,005 | 0,050 | 0,047 | 0,006 | 0,005
 | 16’ | 0,000 | 0,002 | 0,009 | 0,007 | 0,040 | 0,021 | 0,010 | 0,049
Zero baselines results – Identical Receivers with identical firmware
Not considered in the computation : Galileo satellites E18 - E14 - E20

## Slide 9: Results
 |  | GPS L1/Galileo E1 |  |  |  | GPS L5/Galileo E5a |  |  | 
 |  | Mean ISB (m) |  | Std ISB (m) |  | Mean ISB (m) |  | Std ISB (m) | 
 |  | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min
Sept1 – Sept3 | 14’ | 0,023 | 0,027 | 0,018 | 0,017 | 0,078 | 0,058 | 0,036 | 0,029
 | 15’ | 0,004 | 0,002 | 0,003 | 0,005 | 0,044 | 0,042 | 0,007 | 0,012
 | 16’ | 0,003 | 0,003 | 0,016 | 0,017 | 0,034 | 0,037 | 0,008 | 0,016
TRM1 – TRM2 | 14’ | 0,120 | 0,120 | 0,011 | 0,012 | 0,003 | 0,004 | 0,019 | 0,076
 | 15’ | 0,150 | 0,150 | 0,004 | 0,004 | 0,0017 | 0,013 | 0,020 | 0,036
 | 16’ | 0,140 | 0,140 | 0,004 | 0,004 | 0,008 | 0,01 | 0,021 | 0,030
Zero baselines results – Identical Receivers with identical firmware
Not considered in the computation : Galileo satellites E18 - E14 - E20
Same receivers show ISBs different from 0?

## Slide 10: Results
Chart: TRM1 - TRM2
Short baseline | 0.2093 | 0.2385 | 0.2405 | 0.2187 | 0.2336 | 0.2245 | 0.2331 | 0.2726 | 0.2578 | 0.2956 | 0.2707 | 0.2664 | 0.2524 | 0.2599 | 0.2512 | 0.2037 | 0.2521 | 0.29094 | 0.2311 | 0.2473 | 0.2257 | 0.22455 | 0.2465 | 0.2093 | 0.2435 | 0.2799 | 0.259 | 0.25752
Zero baselines results – Identical Receivers with identical firmware
Analysis over the year 2015
Firmware updates ?

## Slide 11: Results
Zero baselines results – Identical Receivers with identical firmware
Analysis over the year 2015
Chart: TRM1 - TRM2
Short baseline | 0.2093 | 0.2385 | 0.2405 | 0.2187 | 0.2336 | 0.2245 | 0.2331 | 0.2726 | 0.2578 | 0.2956 | 0.2707 | 0.2664 | 0.2524 | 0.2599 | 0.2512 | 0.2037 | 0.2521 | 0.29094 | 0.2311 | 0.2473 | 0.2257 | 0.22455 | 0.2465 | 0.2093 | 0.2435 | 0.2799 | 0.259 | 0.25752
New satellites influence?
E26 – E22
E24 – E30
E08 – E09

## Slide 12: Results
Chart: TRM1 - Sept1
Zero Baseline | 0.34246 | 0.40688 | 0.38467 | 0.36871 | 0.3871 | 0.41933 | 0.44132 | 0.37018 | 0.44849 | 0.45749 | 0.46968 | 0.45141 | 0.39633 | 0.42029 | 0.40928 | 0.40028 | 0.3893 | 0.39018 | 0.37023 | 0.45702 | 0.51391 | 0.4881 | 0.46471 | 0.4533 | 0.45036 | 0.44664 | 0.46312 | 0.44461 | 0.44862
Chart: TRM2 - Sept1
Influence of the temperature?
Temperature registered inside the receiver’s room
TRM2 seems to be responsible for the observed variations of the ISBs!

## Slide 13: Results
Zero baselines results – Different Receivers
 |  | GPS L1/Galileo E1 |  |  |  | GPS L5/Galileo E5a |  |  | 
 |  | Mean ISB (m) |  | Std ISB (m) |  | Mean ISB (m) |  | Std ISB (m) | 
 |  | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min
TRM1 – Sept2 | 16a’ | 0,478 | 0,479 | 0,015 | 0,017 | 4,359 | 4,404 | 0,125 | 0,080
 | 16b’ | 0,432 | 0,443 | 0,016 | 0,052 | 4,360 | 4,361 | 0,098 | 0,069
TRM2 – Sept1 | 16a’ | 0,288 | 0,287 | 0,022 | 0,021 | 4,427 | 4,407 | 0,176 | 0,082
 | 16b’ | 0,182 | 0,187 | 0,026 | 0,024 | 4,359 | 4,399 | 0,064 | 0,041
Not considered in the computation : Galileo satellites E18 - E14 - E20
ZB TRM1-TRM2 = 0,19
ZB TRM1-TRM2 = 0,26

## Slide 14: Results
 |  | GPS L1/Galileo E1 |  |  |  | GPS L5/Galileo E5a |  |  | 
 |  | Mean ISB (m) |  | Std ISB (m) |  | Mean ISB (m) |  | Std ISB (m) | 
 |  | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min
TRM1 – Sept2 | 16a’ | 0,478 | 0,479 | 0,015 | 0,017 | 4,359 | 4,404 | 0,125 | 0,080
 | 16b’ | 0,432 | 0,443 | 0,016 | 0,052 | 4,360 | 4,361 | 0,098 | 0,069
TRM2 – Sept1 | 16a’ | 0,288 | 0,287 | 0,022 | 0,021 | 4,427 | 4,407 | 0,176 | 0,082
 | 16b’ | 0,182 | 0,187 | 0,026 | 0,024 | 4,359 | 4,399 | 0,064 | 0,041
Zero baselines results – Different Receivers
Not considered in the computation : Galileo satellites E18 - E14 - E20
Difference of 10 cm in 70 days
Chart: TRM2 - Sept1
Difference of 10 cm in 70 days in 2015

## Slide 15: Results
Zero baselines results – Different Receivers
 |  | GPS L1/Galileo E1 |  |  |  | GPS L5/Galileo E5a |  |  | 
 |  | Mean ISB (m) |  | Std ISB (m) |  | Mean ISB (m) |  | Std ISB (m) | 
 |  | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min | Epochs | 10-min
TRM1 – Sept1 | 14’ | 0,488 | 0,491 | 0,009 | 0,013 | 4,372 | 4,393 | 0,009 | 0,110
 | 15’ | 0,385 | 0,387 | 0,031 | 0,037 | 4,238 | 4,359 | 0,099 | 0,145
TRM2 – Sept3 | 14’ | 0,248 | 0,261 | 0,052 | 0,062 | 4,586 | 4,563 | 0,382 | 0,421
 | 15’ | 0,145 | 0,120 | 0,022 | 0,102 | 4,104 | 4,451 | 0,295 | 0,161
 | 16a’ | 0,278 | 0,292 | 0,062 | 0,038 | 4,321 | 4,238 | 0,276 | 0,250
 | 16b’ | 0,163 | 0,168 | 0,011 | 0,024 | 4,431 | 4,361 | 0,050 | 0,125
Not considered in the computation : Galileo satellites E18 - E14 - E20

## Slide 16: Positioning with ISBs
Precision of the computed positions with Galileo E5a/ GPS L5 in zero baseline
Chart: TRM1 - Sept2
| 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96
Uncorrected | 7.6963 | 5.1457 | 8.3811 | 7.3193 | 8.1552 | 6.3828 | 10.1222 | 8.3273 | 11.5024
Corrected | 0.80864 | 0.78249 | 1.4706 | 0.91823 | 0.93626 | 0.84097 | 1.1592 | 0.98437 | 1.0467
Estimated | 1.7174 | 1.2014 | 1.1799 | 1.5941 | 0.98166 | 1.1851 | 2.7631 | 1.1042 | 2.6441

## Slide 17: Conclusions
ISBs results in zero baseline
  Identical receivers :
    Septentrio receivers : zero value
    Trimble receivers : non zero value + variation in time
      Investigation of the variation : Influence of firmware updates, new Galileo’s satellites and temperature
  Different receivers :
    Variation in time
    Triangle loop
Positioning
  Removing mean ISBs form previous days improve positioning results

## Slide 18: Prospects
Compute phase ISBs
Further investigate GPSL5/GalileoE5a ISB behaviour
Extend this research to other frequencies/GNSS
Tests of the new Septentrio PolaRx5
Study the longer baseline’s ionospheric issues

## Slide 19
Thank you for your attention
Cecile Deprez and Rene Warnant
University of Liege, Belgium