## Slide 1
Title Slide
Navigation
2 Minute Teaser
Elevation validation and geomorphic metric comparison with focus on ASTER GDEM2, SRTM-C, ALOS World 3D, and TanDEM-X
PICO Session - GM3.1/GI3.17/NH4.11
Ben Purinton and Bodo Bookhagen
Institute of Earth and Environmental Science, Universität Potsdam
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
Click to move forward or use the Navigation panel on the left
30 m
< 30 m
Geomorphometry:

## Slide 2
2 Minute Teaser (1/4)
Digital Elevation Models (DEMs) allow the quantitative analysis of the land-surface through Geomorphometry:
Test hypotheses of landscape evolution, geomorphic processes, transient responses, etc.
Hillshade
Slope
Curvature
Stream Network
DEMs and Geomorphology
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 3
2 Minute Teaser (2/4)
Increase in DEM Availability
The past 20 years have seen dramatic increases in the resolution, accuracy, and availability of DEMs from a number of satellite sensors:
Radar (interferometry) – SRTM
Optical (stereogrammetry) – Terra ASTER
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 4
2 Minute Teaser (3/4)
Unlike elevation change studies (glaciology), geomorphometry relies on the accuracy of a single pixel and the relation to neighboring pixels for channel and hillslope analysis
Issue and Study Motivation
Given the widespread availability and resolutions of modern satellite-derived gridded DEMs, which are the most effective for geomorphometric studies?
A.K.A., What to choose in lieu of “high” resolution (VHR) products from GeoEye, Pleiades, IKONOS,…. lidar, etc.?
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 5
2 Minute Teaser (4/4)
Want to see the dirty details? Come by and check it out!
Methods
We assess the state-of-the-art in space DEMs (SRTM, ASTER, ALOS, TerraSAR-X/TanDEM-X) at resolutions of 5-30 m via:
elevation validation (> 300,000 dGPS measurements)
comparison of geomorphic potential (fluvial m/n, slopes, curvatures, Fourier frequency noise detection)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 6
Courtesy, B. Bookhagen
Study Area (1/2)
Study Area
NW Argentina
Atmospheric and vegetation interference on remote sensing are minimal on arid and internally drained Altiplano-Puna Plateau
Plateau
A
A’
Plateau
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 7
Study Area (2/2)
Study Area
Puna Plateau
(A) Study area of dGPS coverage, with focus on (B) Salar de Pocitos within the internally drained Puna Plateau:
Pocitos
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 8
Data (dGPS/DEM) (1/3)
dGPS Data
307,509 dGPS points with vertical and horizontal accuracy < 0.5 m
Collection using Trimble ProXRS receivers (car/backpack)
Kinematic correction in RTKLIB (http://www.rtklib.com), using UNSA permanent station in Salta
Gridding of dGPS data to DEM of interest, taking average of dGPS heights in each pixel
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 9
DEMs – Used
Dataset (short name) | Data Type | Resolution (m) | Source
SRTM C-band (SRTM-C) | Radar / Edited global product | 30 | Public
ASTER GDEM Version 2 (ASTER GDEM2) | Optical / Edited global product | 30 | Public
ASTER L1A Stereopair Stack (ASTER Stack) | Optical / Raw stereopairs | 30 | Public
ALOS World 3D (AW3D5/30) | Optical / Edited global product | 5/30 | Public (30 m) / Commercial (5 m)
CoSSC TerraSAR-X / TanDEM-X (CoSSC TDX) | Radar / Raw interferograms | 10 | Research agreement
TanDEM-X DEM (TanDEM-X 12/30) | Radar / Edited global product | 12/30 | Research agreement
Focus on radar and optical satellite-derived DEMs from SRTM-C, ASTER, ALOS, TerraSAR-X/TanDEM-X, with resolutions of 5-30 m, all released in past five years!
Data (dGPS/DEM) (2/3)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 10
DEMs – Not used
A number of DEMs were also downloaded and/or experimentally generated, but not used in further analysis because of low resolution (SRTMv4.1), or high frequency noise and artifacts, particularly prevalent in single-pass DEMs from optical sensors:
SRTMv4.1 90 m (radar)
SRTM-X 30 m (radar)
RapidEye 12 m (optical)
SPOT6 5 m (optical)
ALOS PRISM tri-stereopair 10 m (optical)
TerraSAR-X/TerraSAR-X pairs 10 m (radar)
Single-CoSSC TerraSAR-X / TanDEM-X processed to 5 m (radar)
Data (dGPS/DEM) (3/3)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 11
Elevation Validation (1/6)
Elevation Validation
30 m DEMs
1-σ < 3.5 m
1-σ > 7 m
Even after meticulous manual generation and stacking of eight raw ASTER L1A stereopair DEMs, vertical error remained high for ASTER products.
SRTM-C, TanDEM-X, and ALOS World 3D all performed comparably at 30 m resolution
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 12
Elevation Validation
30 m DEMs
SRTM-C vertical uncertainty w.r.t. terrain elevation, slope, and aspect
Elevation Validation (2/6)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 13
Elevation Validation
30 m DEMs
ASTER GDEM2 vertical uncertainty w.r.t. terrain elevation, slope, and aspect
Elevation Validation (3/6)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 14
Elevation Validation
< 30 m DEMs
5 m ALOS World 3D and TanDEM-X show best vertical accuracy.
Even single-pass CoSSC TerraSAR-X/TanDEM-X DEMs have excellent vertical accuracy.
1-σ = 1.6 m
1-σ = 2 m
1-σ = 2-4 m
Note difference in count magnitude: ALOS World 3D and CoSSC TDX only cover Pocitos Basin, but TanDEM-X covers almost all dGPS measurements
Elevation Validation (4/6)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 15
Elevation Validation
< 30 m DEMs
12 m TanDEM-X vertical uncertainty w.r.t. terrain elevation, slope, and aspect
Elevation Validation (5/6)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 16
Elevation Validation
< 30 m DEMs
5 m ALOS World 3D vertical uncertainty w.r.t. terrain elevation, slope, and aspect
Elevation Validation (6/6)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 17
Patrick
We now have a number of high quality (low vertical uncertainty) DEMs with resolutions of 5-30 m
Q: How can we test the quality of geomorphic metrics without field measurements of slope, curvature, channel heads, etc.?
1-3 m control DEM (VHR, lidar, etc.)
A: With a transiently adjusting test catchment and field knowledge of geomorphic processes
Geomorphometry (1/9)
Geomorphometric Comparison
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 18
Geomorphometric Comparison
Quebrada Honda Catchment
Catchment within the Pocitos Basin, used for testing geomorphic hypotheses of transient response to migrating knickpoint.
Using highest-quality DEMs only, across a range of resolution:
30 m SRTM-C
30 m TanDEM-X
12 m TanDEM-X
10 m CoSSC TDX
5 m ALOS World 3D
Geomorphometry (2/9)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 19
Geomorphometric Comparison
Chi Plot Channel Analysis
Geomorphometry (3/9)
Stream Power Incision Model (SPIM):
Issue: must calculate slope from noisy DEM data!
Integrate to generate chi plot and find best fitting m/n without the need to calculate slope and do power-law fitting
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 20
Geomorphometric Comparison
Chi Plot Channel Analysis
2 Methods Tested:
Geomorphometry (4/9)
m/n = 0.51-0.56
m/n = 0.53-0.57
Least-squares fit (Perron and Royden, 2013)
Piece-wise fit (Mudd et al., 2014)
Similar m/n value found regardless of DEM resolution or chi plot method
Slightly lower uncertainties from piece-wise fitting for 5 m DEM
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 21
Geomorphometric Comparison
Slope and Curvature Distributions
Geomorphometry (5/9)
Higher slopes downstream of knickpoint in all DEMs.
More outliers with fining resolution, particularly pronounced in curvature measurements.
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 22
Geomorphometric Comparison
Drainage Area-Slope
Geomorphometry (6/9)
Slopes 0.1-0.2 m/m greater downstream
Drainage area at rollover decreases with fining resolution, but converting to hillslope length reveals consistent LH = 109 ± 26 m.
Issue: Known deficiencies with LH estimation from area-slope plots
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 23
Geomorphometric Comparison
Curvature
Geomorphometry (7/9)
Curvature shows large variability with fining resolution, and with sensor type
Is variability in the ALOS World 3D 5 m just noise from this optical sensor?
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 24
Geomorphometric Comparison
2D Fourier Analysis – DEM Noise
Geomorphometry (8/9)
2D Discrete Fourier Transform (2D DFT) of gridded DEM array allows exploration of the frequencies present (Perron et al., 2008).
Here we take 8 km by 14 km rectangular clips from each DEM over the Quebrada Honda and apply the 2D DFT to generate a 1D plot of spectral power versus wavelength.
2D DFT:
Normalize this by the log-binned regression….. (see next slide)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 25
Geomorphometric Comparison
2D Fourier Analysis – DEM Noise
Geomorphometry (9/9)
Note the noise prevalent in 2-8 pixel steps in the optically generated ALOS World 3D 5 m DEM! This is likely causing slope and curvature outliers.
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 26
Conclusions
Elevation validation does not provide a complete picture of DEM accuracy for geomorphology
All DEMs performed equally well for m/n channel analysis at large (catchment) scales
Slope and curvature measurements are partially dependent on resolution, but curvature in particular is dramatically effected by noise
Optical sensors (e.g., ALOS and ASTER) provide less realistic DEMs compared to radar sensors (e.g., TanDEM-X and SRTM-C) in this study area, where lack of clouds and vegetation should make optical remote sensing easy
While stacking can improve DEM quality (e.g., ASTER Stack and TanDEM-X), for fine-scale analysis of hillslope processes “high” resolution is likely still necessary (Pleiades, lidar, etc.)
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry:

## Slide 27
Links / References
Purinton, B., and Bookhagen, B: Validation of digital elevation models (DEMs) and comparison of geomorphic metrics on the southern Central Andean Plateau, Earth Surface Dynamics, 5, 211-237, 2017 (http://www.earth-surf-dynam.net/5/211/2017/)
Perron, J. T. and Royden, L.: An integral approach to bedrock river profile analysis, Earth Surf. Proc. Land., 38, 570-576, 2013.
Perron, J. T., Kirchner, J. W., and Dietrich, W. E.: Spectral signatures of characteristic spatial scales and nonfractal structure in landscapes, J. Geophys. Res., 113, F04003, 2008.
Mudd, S. M., Attal, M., Milodowski, D. T., Grieve, S. W. D., and Valters, D. A.: A statistical framework to quantify spatial variation in channel gradients using the integral method of channel profile analysis, J. Geophys. Res.-Earth, 119, 138-152, 2014.
RTKLIB (dGPS Post-Processing): http://www.rtklib.com
TopoToolbox (Matlab DEM tools): https://github.com/csdms-contrib/topotoolbox
LSDTopoTools (Chi-analysis and other tools): https://github.com/LSDtopotools
DEM Fourier Noise (From this study): https://github.com/bpurinton/DEM_fourier_noise
Title Slide
Navigation
2 Minute Teaser
28 April 2017
EGU2017-4510
Study Area
Data (dGPS/DEM)
Elevation Validation:
Chi Plot (m/n)
Slope, Curvature, Drainage Area
2D Fourier Analysis
Conclusions
Links / References
Area & Data
Analyses
Takeaways
30 m
< 30 m
Geomorphometry: