## Slide 1
Photography: Nick Ford. CC BY-NC-ND 2.0
A coupled modelling framework to assess the hydroecological impact of climate change. Visser et al. 2019. Environmental Modelling and Software, 114, 12–28.
The Impact of Climate Change on Hydroecological Response in Chalk Streams. Visser et al. 2019. Water, 11, 596.
Limited change in the long-term mean masks changes in inter-annual variability;
In the past (on the baseline) there was a probability of a more varied response to low-probability events. In the future, response flatlines;
These changes are projected as early as 2021.
The impact of climate change on hydroecological response in a chalk stream River Nar, Norfolk, England
2019
Annie Visser-Quinn,
Lindsay Beevers and Sandhya Patidar
Water Academy Heriot-Watt University Scotland
PICO spot 4.8
Start

## Slide 2: Menu
Implications
Wider applicability
Definition of terms
Biodiversity matters
Modelling the hydroecological impact of climate change
Click on the boxes with thick borders
Use the arrows to move forward and backwards
Findings: Inter-annual variability
How to interact with the slides
Next
Findings: River health and ecosystem functionality
Findings: Long-term change
Chalk streams
Case study
Methods overview
≡
Press to return to the menu
Press icons to interact
Previous
References

## Slide 3: Definition of terms
Proxy for river health
Lotic-invertebrate index for flow evaluation (LIFE), combines macroinvertebrate functional flow preferences with the (log) abundance of each taxa to determine flow scores, fs.
Functional feeding group | Description
Collector | A broad grouping generally capturing both filterers and gatherers.
Filterer | Filter suspended FPOM from the water column.
Gatherer | Gather FPOM settled on the substrate.
Parasite | Taxa which do not fit into other groups.
Predator | Carnivorous macroinvertebrates which prey on smaller invertebrates.
Scraper | Consumers of food sources attached to the substrate; e.g. algae and biofilm.
Shredder | Shred and consume plant material such as leaf litter and wood.
Hydroecological response and river health
Flow is widely acknowledged as a major determinant of the health of the river ecosystem.
The term river health interchangeable with hydroecological response, and is, arguably, more useful for interpretation.
Functional feeding groups
Describe macroinvertebrate resource consumption. It is their processing of organic matter which facilitates essential ecosystem processes.
Proxy for ecosystem functionality
≡
FPOM and CPOM, fine and coarse particulate organic matter.
Next
Previous

## Slide 4: Biodiversity matters
Biodiversity is the variability among living organisms, within & between species and ecosystems.
Convention on Biological Diversity
Freshwater is considered the most essential natural resource [2]
Biodiversity provides more than aesthetic, cultural and economic benefits. It improves redundancy, enhancing ecosystem resistance and resilience.
Population growth and climate change
Freshwater biodiversity is declining at twice the rate of terrestrial and marine ecosystems combined [1]
Photography: Nick Ford. CC BY-NC-ND 2.0
Ecosystem services
Biodiversity
Environmental pressures
Human well-being
Ecosystem functionality
Concerns about the long-term sustainability of our water resources
≡
Next
Previous

## Slide 5: Modelling the hydroecological impact of climate change
Level 1 – Climate
Level 2 – Hydrology
Level 3 – Ecology
Level 4 – Ecosystem services
Climate change projections
Cascade of uncertainty
*Water temperature ecological model
WT-ECO* model
Hydrological modelling
Altered flow regime
Precipitation
Ecosystem services
Hydroecological response
Hydroecological model
Temperature
Methods investigating hydroecological response have, typically, been qualitative in nature or quantitative with limited scope.
The effect of uncertainty (e.g. parameter, structural, emissions scenario) is rarely considered.
Hydroecological impact, the impact of the flow regime on river ecology
≡
Next
Previous

## Slide 6: Chalk streams
Support uniquely “diverse and fecund ecosystems” [3]
Complex hydrological processes
Chalk streams have a long memory. The impact of flow perturbation (i.e. flood and drought) is in part, determined by the health of the river ecosystem prior to an event.
English chalk streams
“remain in a shocking state of health” [3,4]
Photography: Nick Ford. CC BY-NC-ND 2.0
Next
The chalk is one of England’s principle aquifers, providing 70% of the drinking water in south-east England [3]
Famous for…
Chalk streams are unique to Southern England and Northern France
Cretaceous chalk
Cretaceous chalk
Cretaceous chalk
≡
Previous

## Slide 7: Case study River Nar, Norfolk
Ecology
Peaks of macroinvertebrate activity occur in spring (AMJ), the hatching season, as flow begins to recede, and autumn (OND), as detritus (food) enters the river system.
Hydrology
Groundwater fed from a chalk aquifer
BFI 0.91
Aquifer recharge occurs in the autumn months with flow peaking in January and February
Canalised river banks
Water meadow
“technically infeasible” for the river to meet the ecological requirements of the Water Framework Directive [5,6]
≡
Site of Special Scientific Interest (SSSI)
Chalk sub-catchment 153 km2
From source 24 km
Pressures on the river include:
Physical modification
  Medieval navigation systems
  Domesday mills
  Ornamental estate lakes and water meadows
  Agricultural drainage and more
Sediment ingress
Over-abstraction
Impoundment: Historic mill
Photography: Nick Ford. CC BY-NC-ND 2.0
Hydrology
Ecology
English chalk aquifer
River Nar chalk sub-catchment
River Nar
Study sites
Next
Previous

## Slide 8: Methods
Weather generator. Able to represent climatic variability, allowing low probability events, vital to ecosystem functionality, to be captured more effectively.
UKCP09 probabilistic climate projections
Coupled modelling framework
River health and ecosystem functionality
A range of represented traits maximises the productivity and functionality of the ecosystem.
The hydrological and hydroecological models were parameterised and validated in the course of the development of the coupled modelling framework.
Scenario. IPCC AR4 SRES A1F1 high emissions
Time slices. 2030s (2021-2050), 2050s (2041-2070) and 2080s (2071-2099); 10,000 generations per time slice.
A matrix of macroinvertebrate functional flow preferences (from the LIFE index) and functional feeding groups.
Spring species level macroinvertebrate data, observed from 1993-2014. The data covers periods of very high and low flows, ensuring that response to extremes are captured.
≡
Next
Previous

## Slide 9: Findings: Long-term change
Distribution
Summary statistics
Summary
≡
Summary
The aggregated projections indicate a very limited change in the mean hydroecological response under climate change, assuming a high emissions scenario.
The summary statistics suggest that, by the end-of-century, there may be a restructuring of the macroinvertebrate community response to low-probability events.
Note that, the smaller scale of change observed between the 2030s to 2050s may be explained by the overlap between these two time slices (2041-2050).
The long-term mean may mask significant changes in the inter-annual variability of hydroecological response.
After an initial increase in variance (2030s), standard deviation falls to below the baseline level by the 2080s. This change is suggestive of a minor increase in low probability hydroecological responses by the end of the century.
2For excess kurtosis and skewness, comparisons from baseline to future are not possible, due to differences in sample size (n = 1000 on baseline, n = 10,000 for projections).
1Excess kurtosis is a measure of the combined weight of the tails relative to the normal distribution; for example, a negative value means that more of the dataset is located in the tails than the normal distribution. (Kurtosis is often misinterpreted as a measure of peakedness.)
Indicates the weight is not located in the tails (hence the observed clustering in the PDFs). The change in kurtosis from the 2030s to 2050s is more than half that of the 2050s to 2080s.
All four time-periods are right-skewed. The increase from 2050s to 2080s is almost 3 times that of 2030s to 2050s.
For the baseline, LIFE scores are centred on ~7, i.e. macroinvertebrates have an average flow preference of slow to sluggish
By the 2030s the clustering of LIFE scores reduces, whilst the average LIFE score begins to increase, representing a moderate shift towards higher flow preferences
The trend of increasing LIFE scores continues into the 2080s, where the clustering of LIFE scores can be seen to increase again
The LIFE index is the proxy for hydroecological response and river health.
The long-term changes represents the aggregated LIFE scores over the 30-year time slices for a 99.5% probability of occurrence (assuming a high emissions scenario), a virtually certain outcome under the IPCC definition.
Click the buttons above to navigate.
Next
Previous

## Slide 10: Findings: Inter-annual variability
On the baseline, LIFE scores can be seen to vary from 10.5 to the maximum of 12.
However, the projections for all three future time slices show a plateau at LIFE scores of 12; a varied response becomes almost impossible.
≡
LIFE score
Right: Vertical cross-sections (at specific quantiles) through annual PDFs of LIFE score; the error bars represent the range of values possible for a virtually certain outcome (99.5% probability, assuming a high emissions scenario).
The y-axis (LIFE score) is not fixed.
A large change occurs between baseline and the 2030s, while the change from the 2050s to 2080s is almost negligible.
A small shift in LIFE scores (by time slice) indicates the increased presence of taxa with higher flow scores, though the variability of LIFE score remains broadly unchanged.
∆ Variance (%) | 2030s | 2050s | 2080s
5th percentile | -65 | -52 | -31
Minimum | -92 | -84 | -98
∆ Variance (%) | 2030s | 2050s | 2080s
95th percentile | -92 | -81 | -91
Maximum | -84 | -97 | -83
The change in variance relative to the baseline stands out. The reduction in variance may reach 92% as early as the 2030s.
The tails are essentially the hydroecological response to lower probability extreme events.
LIFE scores plateau to a value of 1, with almost no variance. This change coincides with a notable reduction in the range of values.
Examination of the year-on-year change in hydroecological response provides further clarification on the subtle changes observed over the long-term.
The timing of these major changes in hydroecological response could occur as early as the 2030s, 2021-2050.
This suggests that a major high or low flow event, in the very near future, could result in a hydroecological response very different to the past (baseline period), where there was the probability of a more varied response. By considering the associated uncertainty, we can be virtually certain of this outcome, based on the available information.
Given a potentially highly limited period of preparation, this is of concern for the future health of the River Nar.
Next
Previous

## Slide 11
Findings: River health and ecosystem functionality
This is a functional matrix, a matrix of the functional feeding groups and functional flow preferences. The values indicate the spring annual average number of species fulfilling a given niche.
Baseline observations
Future projections
Press the buttons below for more information.
≡
Several functional feeding group traits potentially unrepresented under extreme conditions.
In terms of functional feeding group, only a limited number of taxa with a range of flow preferences are observed, e.g. scrapers species which may tolerate anything from very low to rapid flows.
Despite these observations, in the short-term, the ecosystem has been able to successfully recover.
The hydrological projections indicated an increase in the probability of both very high and low LIFE scores; this corresponds with standing waters, drought and rapid flows in the functional matrix.
With this reduction in biodiversity, the concomitant decrease in macroinvertebrate adaptability may significantly impact the resilience of the riverine system.
It is evident that almost none of the taxa previously observed in the River Nar would be able to perform their functional roles, long-term, under such environmental conditions.
X Close
X Close
Next
Previous

## Slide 12: Implications
Future projections suggest that variation is greatly reduced, raising real concerns over the resilience of the river ecosystem.
Despite the limited range of the functional feeding groups on the baseline, the River Nar has, to date, been able to adapt to extreme events due to inter-annual variation.
Impacts projected as early as the 2030s
A large part of this low resilience may be attributed to the pressures on the river.
Projections indicate an increasingly vulnerable riverine ecosystem
Analysis of the distributions indicate an increased probability and magnitude of extreme responses, with less internal variability.
The functional matrix revealed that all functional flow preferences are only met at intermediate flows (LIFE 6-8). Under more extreme conditions, they are effectively ‘knocked out’.
Historic mill
Photography: Nick Ford. CC BY-NC-ND 2.0
Sediment ingress
≡
Next
Previous

## Slide 13: Wider applicability
The River Nar is not alone in this, overall, English chalk streams are in a poor state of health, largely for similar reasons. Therefore, our findings are likely to be more widely applicable to the 200+ chalk streams in England.
Right: Pink catchments regularly fall below environmental flow limits.
[3]
Framework applicable to a wide variety of case studies and flow regimes
Previous
Return to start
The decline in river health is not, and should not, be considered a foregone conclusion, there remains the opportunity to intervene via improved river management.
A coupled modelling framework to assess the hydroecological impact of climate change. Visser et al. 2019. Environmental Modelling and Software, 114, 12–28.
The Impact of Climate Change on Hydroecological Response in Chalk Streams. Visser et al. 2019. Water, 11, 596.
Further reading
≡

## Slide 14: References
[1] WWF. Living Planet Report 2016. Risk and Resilience in a New era; WWF International: Gland, Switzerland, 2016.
[2] Vörösmarty, C.J.; McIntyre, P.B.; Gessner, M.O.; Dudgeon, D.; Prusevich, A.; Green, P.; Glidden, S.; Bunn, S.E.; Sullivan, C.A.; Liermann, C.R.; et al. Global threats to human water security and river biodiversity. Nature 2010, 467, 555.
[3] O’Neill, R.; Hughes, K. The State of England’s Chalk Streams; WWF-UK: Surrey, UK, 2014.
[4] Environment Agency; English Nature. The State of England’s Chalk Rivers: A Report by the UK Biodiversity Action Plan Steering Group for Chalk Rivers; Environment Agency: Bristol, UK, 2004.
[5] Norfolk Rivers Trust. The River Nar—A Water Framework Directive Local Catchment Plan; Norfolk Rivers Trust: Norfolk, UK, 2014.
[6] Rangeley-Wilson, C. The River Nar—A Water Framework Directive Local Catchment Plan; Norfolk Rivers Trust: Norfolk, UK, 2012.
≡