## Slide 1: Optical clocks for gravity field observation and further geodetic applications
Hu Wu, Jürgen Müller, Annike Knabe
Institut für Erdmessung (IfE), Hannover
EGU Generally Assembly
May 4-8, 2020

## Slide 2: Clocks for space gravimetry / Scenario 1
Potential value
Space-to-ground clock comparison
Reference clock
LEO satellite Clock
Notes: Ground clocks: a number of ground clocks are requiced to transmit their potential values to the LEO clock via the link between geostationary clocks
LEO clock: to observave the potential value of the Earth gravity field through measuring the potential differences w.r.t. ground clocks
The goal is to obtain a gravity potential values with a global and homogeneous coverage for the global gravity field recovery.

## Slide 3: Clocks for space gravimetry / Scenario 1
One-month GRACE satellite A orbit (January 2006)
@ ~475 km
sampling rate: 5 s
Degree-error RMS in geoid height
Clock error only

## Slide 4: Clocks for space gravimetry / Scenario 2
LEO satellite clocks
Potential difference
Space-to-space clock comparison
Notes: In addition to the one-single LEO satellite clock, we also consider a mission concept similar to GRACE, which apply a-pair LEO satellite to measure the potential differences. It is a kind of differential measuring concept.
Theoretically, this mission concept does not need ground clocks, and much easier to obtain observations with a global and homogenous spatial coverage.

## Slide 5: Clocks for space gravimetry / Scenario 2
One-month GRACE satellite A & B orbit (January 2006)
@ ~475 km
sampling rate: 5 s
Degree-error RMS in geoid height
Clock error only
Notes: Solid curves represent coefficient differences w.r.t. EIGEN-6c4;
Dashed curves represent formal errors;

## Slide 6: Mass loss in Greenland
A
Clock uncertainty: 10-18
A
A
B
B
Clocks can detect the mass loss in some areas. Being complementary to GRACE, clocks provide:
point-wise and
high-frequency sampling obs.

## Slide 7: Height system unification
Clocks are powerful in obtaining height differences between distant points. This makes them appropriate for height system unification, by identifying:
discrepancies (offsets) between different height datums;
systematic distortions of national/regional levelling networks.
Notes: In addition, clocks can be used to control at tide gauges and connect islands or remote areas where levelling is not possible.

## Slide 8: Space geodetic reference frame
Gravity potential at different altitudes
Gravity field above the equator at different altitudes
Potential: [m2/s2]
Notes: The effect of temporal gravity field can be ignored;
The natural disaster can destroy the gound-based reference frame. But their influence on the space-based reference frame will be tiny. Therefore, the space-based reference frame is easily maintainable.
Satellites in a higher altitude can cover a large area. Several satellite in such orbits are able to cover the whole earth.
The gravity field is much regularer in higher altitudes, e.g., the navigation satellite or geostationary orbit.

## Slide 9: Space geodetic reference frame
Clocks in higher orbits support realizing a global gravity or height reference system, which is:
stable/robust over time;
easy to maintain.
Notes: The effect of temporal gravity field can be ignored;
The natural disaster can destroy the gound-based reference frame. But their influence on the space-based reference frame will be tiny. Therefore, the space-based reference frame is easily maintainable.
Satellites in a higher altitude can cover a large area. Several satellite in such orbits are able to cover the whole earth.

## Slide 10: Summary
For gravity field determination, clocks:
  deliver the gravity potential (difference), which is a scalar quantity and robust to attitude errors;
  are assumed for space gravimetric obsevations in two scenarios, and show the highest sensitivity to low-degree gravity field signals.
As further geodetic applications, clocks can:
unify local height systems;
monitor mass changes like in Greenland;
realize a global gravity/height reference system.