## Slide 1: Experimental Modelling of Black Carbon Emissions from Gas Flares in the Oil and Gas Sector
Parvin Mehr
NSERC FlareNet Strategic Network
Energy and Emissions Research Lab.,
Dept. of Mechanical and Aerospace Engineering,
Carleton University, Ottawa, Canada
Parvin Mehr, Bradley M. Conrad, Matthew R. Johnson

## Slide 2
This video gives a brief back ground about black carbon and why it’s important to quantify its contribution to climate change.
Play me!

## Slide 3: Aim and objectives
Objective:
  Investigate the effect of key aerodynamic parameters, flame regimes, and fuel compositions on BC yield trends in turbulent diffusion flames of practical interest;
  Evaluate practical methods to model and predict BC emissions from this critically important atmospheric source.

## Slide 4: Experimental Setup & Method
Conrad & Johnson 2019
MFC
MFC
Filt.
Filt.
*
*
*
This figure shows a simplified schematic of Carleton University Flare Facility (CUFF).
Gas-phase fuels were flow-controlled using Mass Flow Controllers (MFCs) calibrated to high-accuracy.
Liquid-phase fuels were flow-controlled using Coriolis flow meters, evaporated and mixed with a methane carrier gas, and forwarded to a fuel mixing chamber via a heated line (maintained at ~80°C).
Gases (C1-C4)
Liquids (C5-C7)
Heated Line
MFCs

## Slide 5: Experimental Setup & Method
OCEC
*
Fume hood
Flare stack (12.7-76.2mm)
Fuel mixtures were then forwarded to vertically oriented flare stacks of 12.7 - 76.2 mm in internal diameter. Combustion products mixed with diluent air were captured by a fume hood.
To quantify BC yield a thermal-optical organic/elemental carbon (OCEC) instrument (Sunset Labs model 4) was used to analyze diluted combustion products extracted from the exhaust duct.
To prevent overload of the solid-phase instrument, extracted combustion products were optionally diluted further in a sampling tunnel.

## Slide 6: Flare Gas Composition
Jurisdiction | Fuel ID | C1 | C2 | C3 | nC4 | iC5 | nC6 | nC7 | N2 | CO2 | MW [g/mol] | HHVV [MJ/m3] | CHR [−]
Alberta | AB-L | 92.39 | 0.32 | 0.09 | 0.40 | 0.06 | 0.03 | 0.03 | 1.54 | 5.16 | 17.98 | 37.73 | 0.253
 | AB-M | 86.36 | 6.83 | 2.36 | 0.97 | 0.33 | 0.13 | 0.18 | 1.62 | 1.22 | 19.03 | 43.81 | 0.271
 | AB-H9 | 75.68 | 11.52 | 6.06 | 2.60 | 0.78 | 0.23 | 0.21 | 1.70 | 1.22 | 21.77 | 49.54 | 0.290
 | AB-H6 | 75.16 | 11.44 | 6.02 | 4.48 | - | - | - | 1.69 | 1.21 | 21.76 | 46.53 | 0.290
Bakken | BK-1 | 49.12 | 20.97 | 15.04 | 6.72 | 2.15 | 0.87 | 0.78 | 3.66 | 0.70 | 29.13 | 64.33 | 0.329
 | BK-2 | 57.78 | 19.97 | 11.35 | 3.81 | 0.93 | 0.22 | 0.15 | 5.22 | 0.57 | 25.22 | 55.19 | 0.310
Ecuador | EC-O2 | 58.89 | 7.80 | 9.29 | 5.19 | 2.18 | 0.89 | 0.81 | 5.75 | 9.20 | 27.71 | 51.54 | 0.315
 | EC-O3 | 40.82 | 8.16 | 16.93 | 14.75 | 6.81 | 2.06 | 1.38 | 3.37 | 5.71 | 36.57 | 75.17 | 0.355
 | EC-O4 | 55.22 | 7.63 | 11.65 | 8.79 | 3.95 | 1.37 | 0.94 | 4.12 | 6.31 | 30.31 | 60.92 | 0.331
North Sea | NS-A | 82.48 | 8.09 | 4.06 | 1.53 | 0.40 | 0.16 | 0.15 | 1.43 | 1.70 | 20.07 | 45.65 | 0.278
Russia | RU-G1 | 73.96 | 3.08 | 7.87 | 6.79 | 2.35 | 0.63 | 0.57 | 1.90 | 2.85 | 24.80 | 54.15 | 0.306
 | RU-G2 | 77.05 | 5.29 | 8.24 | 4.28 | 1.24 | 0.30 | 0.27 | 1.56 | 1.76 | 22.72 | 51.07 | 0.295
Experimental | CH4 | 100.00 | - | - | - | - | - | - | - | - | 16.04 | 37.67 | 0.250
 | CH4/C3H8 | 50.00 | - | 50.00 | - | - | - | - | - | - | 30.07 | 65.76 | 0.333
This table summarizes the studied flare gas compositions alongside key relevant metrics: molecular weight (MW), volumetric higher heating value (HHVv), and carbon-hydrogen ratio (CHR).
Twelve flare gases sourced from field measurements in five globally relevant oil and gas jurisdictions.
Two additional, easily replicated fuel mixtures, pure methane and an equal mixture by volume of methane and propane.

## Slide 7: Test Conditions
To evaluate the effect of aerodynamic parameters on BC yield, the regime map of Delichatsios [1] was used as a guideline for the design of the conditions tested.
The flowrate and diameters were selected so that the resulting Re and Frg coordinates would encompass the shaded inclined rectangle in this figure, and thereby closely approximate the estimated aerodynamic regime of typical UOG flares.

## Slide 8: Soot yield calculations and Uncertainty analysis
To compute BC yield () with precisely quantified uncertainties at the CUFF, simultaneous and accurate knowledge of three data is required:
Volumetric dilution factor of the diluted combustion products as they enter the solid-phase sampling and dilution tunnel
  quantified using a CO2-balance on the sampling and dilution tunnel, with CO2 quantities measured using a non-dispersive infrared detector (LI-COR LI-850).
And the volumetric dilution factor of the raw combustion products as they are captured into the fume hood.
Carbon mass concentration in the solid-phase sampling and dilution tunnel, obtained by measuring:
  the carbon mass present in the extracted sample using the OCEC and,
  the sampled volume with a high-accuracy thermal mass flowmeter (Bronkhorst EL-FLOW Prestige).
Notes: A detailed uncertainty analysis was conducted using the Monte Carlo method. And both bias and precision were considered.
To compute BC yield (𝑌_𝐵𝐶) with precisely quantified uncertainties at the CUFF, simultaneous and accurate knowledge of three data is required:
Carbon mass concentration in the solid-phase sampling and dilution tunnel (𝜚_𝐵𝐶, [g/m3]), which was obtained by measuring the carbon mass present in the extracted sample using the ocec and measuring the sampled volume with a high-accuracy thermal mass flowmeter (Bronkhorst EL-FLOW Prestige).
Volumetric dilution factor of the diluted combustion products as they enter the solid-phase sampling and dilution tunnel (𝛿_1, [−]), which was quantified using a CO2-balance on the sampling and dilution tunnel, with CO2 quantities measured using a non-dispersive infrared detector (LI-COR LI-850).
And the volumetric dilution factor of the raw combustion products as they are captured into the fume hood (𝛿_2, [−]) which was quantified using the carbon-balance method of Corbin & Johnson [9], in which volume fraction measurements of gas-phase carbonaceous species in the exhaust duct and ambient background were obtained using cavity ring down instruments (Los Gatos, various models). These data enabled calculation and comparison of the molar flow rate of the duct with the controlled molar flow rate of the flare gas to directly yield the dilution factor.

## Slide 9: Accounting for deposition losses
FlareNet Particle Penetration Calculator (FPPC)-a program written in collaboration with UBC- can quantify and account for sampling losses from various mechanisms.
Allows robust quantification of measurement uncertainties and is an essential component of developing scientifically defensible particulate matter emission factor data and models.
Notes: Aerosol instruments are reliant on the sampling lines that feed them, where sampling lines with different attributes such as diameter and length can affect particle deposition within the lines and hence change the output of the instruments at the end of the line.

## Slide 10: Some of the Loss Mechanisms
Thermophoresis
Inertial Deposition in Bend
Diffusion
Gravitational Settling
Temperature gradient drives particles from hot gas toward cold wall
Asymmetric pressure on particle from molecules from hot/cold parts of the flow.
Momentum / inertia of large particles prevents transport through bends
Increased losses for higher velocities and larger particles
Diffusion of particles driven by concentration gradients
Important loss mechanism for small particles
Gravitational settling of particles
Important loss mechanism for large particles moving at slow velocity
Notes: These are some of the loss mechanisms incorporated in the code. The principle driving forces for these mechanisms are gravitational, inertial and diffusive. they are potentially important depending on the particle size distribution. generally speaking, larger particles are more strongly influenced by gravitational and inertial forces, whereas smaller particles with higher diffusion coefficients are more easily lost due to diffusion.

## Slide 11: Mass loss quantification
FlareNet Mass Loss Calculator (FMLC): uses the fitted particle penetration curves calculated with FPPC program to calculate mass losses of different flare condition.
Flaring condition + sampling line properties
Particle loss/penetration for each instrument
Raw SMPS data
Mass loss
FMLC
FPPC
Fitted curve coefficients
Notes: After calculating particle losses and penetration for each instrument using FPPC program, FMLC was created to quantify mass losses. For running the program, the user should provide the fitted curves coefficients of the penetration in the excel input folder for different dilution conditions and the raw data from the one point of the instrument measurements (SMPS).

## Slide 12: Mass Loss %
This table summarizes the results from the program. we particularly were interested in the ECOC losses since that’s the main instrument that we use to quantify BC.

## Slide 13: Comparison To literature (I)
The operating conditions for the current data plotted on the non-dimensional map suggested by Delichatsios [1], as well as data found in literature (updated from [2]).
Current soot yield data spans the “transition buoyant” and “transition shear” regimes defined by the solid diagonal line.
A comparison of SGE data for flames from Becker and Liang [3] and corresponding results from the current work.
Values measured by Becker and Liang [3] are approximately an order of magnitude larger. This is most likely due to:
  Different flow conditions,
  Fuel compositions and,
  Differences in sampling protocols.

## Slide 14: Comparison To literature (II)
A comparison of SGE versus τr* for flames from [3,4] and results from the current tests:
  Becker and Liang’s [3] data appear to show upward trends with increasing τr* whereas the present data do not show any clear trend.
Fire Froude number suggested by Delichatsios [1] was also tested in an attempt to scale soot yield values.
There is a trend similar to Becker and Liang [3] among the data.
The data for propane and ethylene of Sivathanu and Faeth [4] seem to complete the trend of Becker and Liang [3].
Becker and Liang [3] calculated τr* from their measured flame length, whereas Sivathanu and Faeth [4] measured residence time via flame photography.

## Slide 15: Scaling BC [g/Kg]
Three controlled variables:
  the fuel velocity,
  the burner exit diameter, and
  the fuel.
Froude number
  Volumetric Air to Fuel ratio (AFv),
  Carbon to Hydrogen ratio (CHR),
  Mean number of Carbon in Hydrocarbons (C#),
  Stoichiometric mixture fraction (S) and,
  the temperature ratio defined as:

## Slide 16: Scaling BC (I)
The percentage error (E%) of each model was defined as:
This figure shows some of the combinations tested for the 25.4mm burner.
It can be seen that both models are left skewed. However, is the more suitable scaling parameter among the tested combinations, since it has a lower range of percentage error (±30%).
Notes: This figure shows some of the combinations tested for the 25.4mm burner. It can be seen that there is not much of a difference between the two figure however, the suitability of the model is defined based on its predicting capabilities. Curve fitting in MATLAB, it is apparent that the statistical parameters that define the goodness of fit are better in the LHS figure. The percentage error (E%) of each model was defined as:
Where 〖BC yield〗_actual are the experimental values whereas, 〖BC yield〗_theoretical are values calculated from the fitted equation. Figure 4.3.2c and d show the histogram of E%. It can be seen that both models are skewed left. However, Fr^2 T_ratio/AF_𝑣 〖C#〗^2 is the more suitable scaling parameter among the tested combinations, since it has a lower range of percentage error (±30%).

## Slide 17: Scaling BC (II)
3D plot of emissions scaled by and separated by diameters in the third axis
Only the 25.4mm burner has the full spectrum and other diameters are incomplete due limitation of CUFF
  Model inconclusive and unsuitable to use.
  The steep ramp up at lower scaling parameter values and the flat shape of the curve as the scaling parameter approaches infinity, points out that two different regions may exist
Data can possibly be scaled better if separating the two regimes as suggested by Delichatsios [1].

## Slide 18: Scaling BC (Transition Buoyant)

## Slide 19: What does it mean?
Mixing area

## Slide 20: Scaling BC (Transition Shear)

## Slide 21: What does it mean?
Mixing length

## Slide 22: Scaling BC Rate (Transition Buoyant)
In transition buoyant regime, as defined by Delichatsios [1], BC (when corrected by carbon number) simply scales with mass flow rate.

## Slide 23: Scaling BC Rate (Transition Shear)

## Slide 24: What does it mean?
1/Mixing time
Turbulent mixing coefficient (eddy diffusivity)
Mixing length
Notes: n the right hand side of 𝑉_𝑒/𝐿_𝑓 can be interpreted as the inverse of mixing time and 〖D_𝑒〗^3/〖L_𝑓〗^0.646 as the mixing volume such that:Note that shear flames are S-shaped and therefore the length used in calculating the volume would not be same as the flame length which explains the term D_𝑒/〖L_𝑓〗^0.646 .
So when we flatten a S curve what’s the ratio of the length of that curve to say flame length…not sure of the wording of this section-need help.
Another approach to explaining the physics behind the obtained model is taking the 〖D_𝑒〗^2/(L_𝑓/V_𝑒 ) term as the turbulent mixing coefficient (eddy diffusivity) [7] and D_𝑒/〖L_𝑓〗^0.646 as the mixing length. Therefore,
which again suggests that the emission rate (corrected by carbon number for different fuels) in the transition shear regime is simply scaled by the mixing rate.

## Slide 25: Modified regimes
In an attempt to find a better model with lower range of E%, regimes defined by Delichatsios [1] were slightly modified.
Delichatsios himself in [1] points out that there is some fuzziness in the determination of the lines, not only because of uncertainties concerning the location of the lines, but also because he does not include situations which involve instabilities and oscillations of the flames.

## Slide 26: Scaling BC Rate (Modified Transition Buoyant)
The dashed blue line in this figure shows the new limit for transition buoyant going to transition shear regime.
Not surprisingly, the range of E% increases from ±24% to ±30%.
Still scales with flowrate!

## Slide 27: Scaling BC Rate (Modified Transition Shear)
What does it mean?
The range of E% decreases from ±28% to ±21%.

## Slide 28: Comparison to Current emission factors
The current emission factors lie in the region between the AB-M and BK-1 flare gases.
This suggests that these emission factors were based on flare gas compositions containing similar hydrocarbons to the flare gases of the current work.
The CAPP factor predicts a soot yield value much higher than those measured in the current work- for flare gases shown which have heating values in the range of 43-64 MJ/m3.
This suggests that the application of this factor to flares in the upstream energy industry with nominal heating value of 45 MJ/m3 is questionable.
Comparison of EFs from the literature with current results a)Buoyant b) Shear c) Modified buoyant d) Modified shear

## Slide 29: References
[1] M.A. Delichatsios, Transition from momentum to buoyancy-controlled turbulent jet diffusion flames and flame height relationships, Combust. Flame. 92 (1993) 349–364. doi:10.1016/0010-2180(93)90148-V.
[2] J.D.N.B. carbon particulate matter emission factors for buoyancy-driven associated gas flares McEwen, M.R. Johnson, Black carbon particulate matter emission factors for buoyancy-driven associated gas flares, J. Air Waste Manag. Assoc. 62 (2012) 307–321. doi:10.1080/10473289.2011.650040.
[3] H.A. Becker, D. Liang, Total emission of soot and thermal radiation by free turbulent diffusion flames, Combust. Flame. 44 (1982) 305–318. doi:10.1016/0010-2180(82)90080-3.
[4] Y.R. Sivathanu, G.M. Faeth, Soot volume fractions in the overfire region of turbulent diffusion flames, Combust. Flame. 81 (1990) 133–149. doi:10.1016/0010-2180(90)90060-5.