## Slide 1
Recovering P from a eutrophic lake via hypolimnetic withdrawal and purification: Summary
Soila Silvonen1, Juha Niemistö1, Leena Nurminen1, Anne-Mari Aurola2, Ismo Malin3, Matti Kotakorpi3, Jukka Horppila1, Tom Jilbert1
A simple water purification system allows P to be harvested from the hypolimnion of eutrophic lakes

## Slide 2: Recovering P from a eutrophic lake via hypolimnetic withdrawal and purification
Soila Silvonen1, Juha Niemistö1, Leena Nurminen1, Anne-Mari Aurola2, Ismo Malin3, Matti Kotakorpi3, Jukka Horppila1, Tom Jilbert1
1 University of Helsinki, Viikinkaari 1, P.O. Box 65, 00014, University of Helsinki, Finland
2 AFRY, P.O. Box 50, FI-01621 Vantaa, Finland
3 City of Lahti, Askonkatu 2 FI-15100 Lahti, Finland
Photo: J. Horppila

## Slide 3: P and eutrophication of lakes
P runoff into lakes is a significant factor in lake eutrophication, which manifests itself as e.g.
  Harmful algal blooms
  Fish kills
P accumulated in lakes can be considered “lost”, out of reach – problematic, as P is a finite resource
Globally, the annual accumulation of P in lakes is 1-3.1 Tg (106 tonnes) (Bennett et al. 2001)
Photo: S. Silvonen

## Slide 4: Hypolimnetic withdrawal – removing P from lakes
Conventional withdrawal
Principle: P-rich water is led downstream from the lake
Widespread approach (Nürnberg, 2007)
Closed purification circuit
P-rich water is pumped into a P-capturing unit and back into the same lake
Hardly any documented instances, under development
P
P
P
P
P
P
P
Sediment
Hypolimnion
Withdrawal pipe (Olszewski tube)
P
Lake outflow
P
P
Background: In thermally stratifying lakes, P typically accumulates in near-bottom water (hypolimnion) due to different release mechanisms from sediment, and decomposition of settling organic matter
P
P
P
P
P
P
P
Sediment
Hypolimnion
Withdrawal pipe (Olszewski tube)
P
Water purification unit

## Slide 5: Study questions
Is it possible to remove and capture significant amounts of P from a lake with a simple water purification unit?
How P-concentrated can the material extracted in such a system be?
What are the possible forms in which P can be captured?

## Slide 6: Study methods
Source of map: National Land Survey of Finland
Study site: Lake Kymijärvi (Southern Finland) – small (~6 km2) boreal dimictic lake
A pilot version of a hypolimnetic withdrawal and purification system built in 2018
Photo: J. Horppila
Photo: J. Horppila
Treatment unit
Filter

## Slide 7
P-rich hypolimnetic water withdrawn
P precipitation by
a) Fe oxides from aerated lake water, or
Ca(OH)2
Silo
b) Ca(OH)2 added from a chemical silo
-> hydroxyapatite
P-rich precipitate captured in filters
Filtered water flows back into the lake via a wetland
Functioning of the system

## Slide 8
2017: Preliminary investigations on the potential for P removal in study lake during thermal stratification:
  P content of sediment and accumulation in pore water
  P accumulation in hypolimnetic water
2018 & 2019: Test runs of hypolimnetic withdrawal and purification system pilot:
  Two P precipitation pathways: water aeration (Fe precipitation) and Ca(OH)2 addition (hydroxyapatite Ca5OH(PO4)3 formation)
  Two parallel filter materials (calcitic & non-calcitic sand/gravel)
  Data collection: water samples (P capture), solid material from filters (P concentration and association with Fe/Ca in precipitate)

## Slide 9: Results
Chart: Sediment depth (cm)
| 1420 | 2490 | 3080 | 3860 | 4130 | 4160 | 4340 | 4500 | 4390 | 4180 | 4000 | 3970 | 3810 | 4060 | 3780
22 August | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29
P accumulation in the hypolimnion
22.8.2017
Water column
Sediment pore water
P diffusive flux from sediment into water
From: Boudreau (1997)
D = temperature-corrected diffusion coefficient of H2PO4-
dC = P concentration difference between surface sediment pore water and near-bottom water
dz = diffusion distance
Θ = tortuosity
Chart: mg P m-2 d-1
| 9.5. | 5.6. | 5.7. | 2.8. | 22.8. | 12.9.
5 m | 0.10793 | 0.27216 | 2.1244 | 3.0184 | 1.1088 | 0.59072
7 m | 0.40374 | 2.9828 | 9.1871 | 8.2981 | 3.3213 | 4.1115
8.8 m | 2.2987 | 5.5184 | 7.6792 | 4.7988 | 7.4015 | 5.1262
Chart: Water depth (m)
| 0-1 | 1-2 | 2-3 | 3-4 | 4-5 | 5-6 | 6-7 | 7-8 | 8-8.8
TP | 37.2 | 35.5 | 34.6 | 31.4 | 37.1 | 47.9 | 52.1 | 92.9 | 300
SRP | 4.48 | 3.63 | 2.26 | 6.72 | 6.24 | 10.3 | 7.98 | 36.3 | 159

## Slide 10
Water aeration only
1 Pre-treatment tap
2 Treatment well (aeration/Ca(OH)2 addition)
3 Non-calcitic gravel, inflow
4 Calcitic sand, inflow
5 Non-calcitic gravel, outflow
Ca(OH)2 addition
Test runs of hypolimnetic withdrawal and purification system: P retention (water samples)
P retention in filters
TP: 85%
SRP: 97%
P retention in filters:
TP: 75%
SRP: 94%
6 Calcitic sand, outflow
7 Post-filter well
8 Wetland inflow
9 Wetland 1, 1.5 m
10 Wetland 2, 1.5 m
11 Wetland outflow
Sampling points

## Slide 11
Chart: 4.7.2019
| 0-20 | 20-40 | 40-60 | 60-80
P from filter material | 537.6514 | 519.9523 | 496.0892 | 411.5384
Precipitated P | 1333.5351 | 1985.9346 | 5161.8416 | 12488.062
Chart: 22.8.2019
| 0-20 | 20-40 | 40-45
P from filter material | 425.186 | 405.5983 | 403.5708
Precipitated P | 1303.3753 | 1594.3833 | 2422.5272
Chart: 9.8.2019
| Fe-P | Ca-P | Residual HNO3 digest
 | 5225.8697 | 219.4341 | 585.7755
Water aeration only Filter material: Non-calcitic sand/gravel
V of water flowed through: 2088 m3
Chart: 22.8.2019
| Fe-P | Ca-P | Residual HNO3 digest
 | 1415.5394 | 2148.7753 | 61.6437
Ca(OH)2 addition Filter material: Non-calcitic sand/gravel
V of water flowed through: 194 m3
TP
P fractions
Test runs of hypolimnetic withdrawal and purification system: P content of extracted material
Coring sample from filter
Photo:T. Jilbert

## Slide 12: First conclusions
There is great potential in eutrophic lakes for harvesting P from hypolimnetic water
A simple purification system based on P precipitation and filtering effectively removes P from water
Different precipitation mechanisms may be equally effective, but they will affect the composition of the captured material – including the form of P

## Slide 13: Thank you for your interest!
Cited literature:
Bennett, E. M., Carpenter, S. R., & Caraco, N. F. (2001). Human impact on erodable phosphorus and eutrophication: a global perspective: increasing accumulation of phosphorus in soil threatens rivers, lakes, and coastal oceans with eutrophication. BioScience, 51(3), 227-234.
Boudreau, B. P. (1997). Diagenetic models and their implementation. Springer.
Nürnberg, G. K. (2007). Lake responses to long-term hypolimnetic withdrawal treatments. Lake and Reservoir Management, 23(4), 388-409.
Photo: J. Horppila