## Slide 1: Anthropogenic salinization of naturally dilute boreal lakes in Finland
1Mira Tammelin, 2Tommi Kauppila, 2Jari Mäkinen
1University of Turku / Finnish Environment Institute
2Geological Survey of Finland
D540, EGU2020-1344
@MiraTammelin

## Slide 2: Motivation
PhD project:
Spatial variability in natural trophic states of Finnish lakes and their anthropogenic eutrophication
Increases in
electrical conductivity (proxy for salinity)
common in addition to eutrophication
Articles about widespread freshwater salinization start to appear
Freshwater salinization is an emergent threat in the Northern Hemisphere
Is salinization affecting also dilute boreal lakes?
Kaushal et al. 2018.
PNAS 115:E574-E583
@MiraTammelin
1
2
3
4
Causes of salinization:
Irrigation
Water abstraction
Resource extraction
Accelerated weathering
Road de-icing
Sewage
Cañedo-Argüelles et al. 2018.
Phil. Trans. R. Soc. B 374:20180002

## Slide 3: Study sites
Basin | Min | Md | Max
Average depth (m) | 0.7 | 2.6 | 8.3
Lake surface area (km2) | 0.004 | 2.6 | 114
Catchment area (km2) | 0.2 | 31 | 5564
51 sites
82-160 m a.s.l.
19 sites
15-111 m a.s.l.
Modern water quality | Min | Md | Max
Electrical conductivity (mS m-1) | 0.5 | 5.2 | 17
pH | 5.5 | 7.1 | 9.3
Total phosphorus (µg l-1) | 3.0 | 43 | 228
Total nitrogen (mg l-1) | 0.15 | 0.78 | 3.60
Color (mg Pt l-1) | 5.0 | 93 | 340
Catchment land use (%) | Min | Md | Max
Forest | 25 | 75 | 86
Agriculture | 0 | 12 | 56
Built areas | 0 | 3 | 23
Wetland | 0 | 2 | 9
Water | 1 | 9 | 30
(granitic/gneissic)
Slowly weathering bedrock
 Dilute lakes
@MiraTammelin
GTK open license CC BY 4.0, modified from GTK’s Superficial deposits of Finland 1:1 000 000 data, imported from Hakku service on 3 July 2019. Original material: https://hakku.gtk.fi/en
Summarizations in the tables are based on Pintavesien tilan tietojärjestelmä, vedenlaatu PIVET and Corine Land Cover 2012 of the Finnish Environment Institute (CC BY 4.0). Original data: https://www.syke.fi/en-US/Open_information
N

## Slide 4: Methods
Post-disturbance conditions (top samples)
  Taken with Limnos gravity corer
  From sediment surface
Pre-disturbance conditions (bottom samples)
  Taken with rod-operated piston corer
  Sample depths based on magnetic susceptibility profiles of sediment cores (2 samples, 10 cm apart)
Top-bottom sediment sampling
Magnetic susceptibility
Proxy for intensified catchment erosion
Often the first sign of human impact
Diatom assemblages
Ordinations
  Ecologically important water quality variables
  Pre- to post-disturbance change
WA-PLS regression
  Based on: Post-disturbance water quality + diatoms
  Input: Pre-disturbance diatoms
  Output: Pre-disturbance epilimnetic electrical conductivity
  Identified from top & bottom samples
Quantitative paleolimnology
Diatoms (phytoplankton)
Sediment coring
@MiraTammelin
Human
disturbance

## Slide 5: Results – Natural variability
Pre-disturbance electrical conductivity (EC) very low
Lower EC in till-rich inland
Higher EC on clayey coast
Tammelin et al. 2017.
Hydrobiologia 799:309–325
Tammelin et al. 2018.
Front. Ecol. Evol. 6:65
Tammelin et al. In prep.
Pre-disturbance EC correlation with |  | 
 | r | p
Glacial till | -0.62 | < 0.001
Clay | 0.54 | < 0.001
Bedrock outcrops | 0.39 | 0.001
Water | 0.33 | 0.005
Peat | -0.25 | 0.035
Sand & gravel | 0.25 | 0.040
@MiraTammelin

## Slide 6: Results – Salinization
EC important driver of modern diatom assemblages
Pre- to post-disturbance EC increase in 61/70 sites
  Average increase 3.0 mS m-1
  Maximum increase 11.7 mS m-1
Average EC increased 65% from 3.8 to 6.3 mS m-1
Coastal region more affected than inland
  Land use more intense in southern Finland
Sites in the order of increasing pre-disturbance EC
@MiraTammelin

## Slide 7: Take home message
Finnish lakes very dilute in natural conditions (< 7.5 mS m-1)
  Small-scale natural variability related to catchment geology
Dilute boreal lakes also threatened by salinization
   Need for management!
@MiraTammelin

## Slide 8: Acknowledgements
Travel grant for EGU2020
Research funding
@MiraTammelin

## Slide 9
Thank you!
@MiraTammelin