## Slide 1: Which method should we use to draw empirical rainfall thresholds for landslide early warning?
David J. Peres
Antonino Cancelliere
Department of Civil Engineering and Architecture University of Catania
© Copyright by the Authors

## Slide 2: Empirical rainfall thresholds for landslide early warning
Rainfall is the main cause of landslides
Early warning of landslides can save lives
Rainfall thresholds linked to landslide occurrence are an important component of landslide early warning systems
Thresholds are commonly expressed in terms of a power-law linking rainfall event duration and intensity

## Slide 3: After collecting the data on landslide events…
Rainfall event intensity
Rainfall event duration
Triggering events

## Slide 4: After collecting the data on landslide events…
Rainfall event intensity
Rainfall event duration
Lower limit by eye
Triggering events

## Slide 5: After collecting the data on landslide events…
Frequentist P:
More objective
than “by eye”
Regression
5 % non-exceedance thresholds
Triggering events

## Slide 6: After collecting the data on landslide events…
Frequentist P:
More objective
than “by eye”
5 % non exceedance thresholds
Triggering events

## Slide 7: After collecting the data on landslide events…
Non-triggering events

## Slide 8: After collecting the data on landslide events…
Frequentist N
Non-triggering events
Regression

## Slide 9: After collecting the data on landslide events…
Frequentist N
Non-triggering events
5 % exceedance threshold
This method is rarely used

## Slide 10: After collecting the data on landslide events…
Optimize
a given objective
in terms of the
ROC matrix
Triggering and
Non-triggering

## Slide 11: After collecting the data on landslide events…
Optimize
a given objective
in terms of the
ROC matrix
Triggering and
Non-triggering
Frequentist N
Frequentist P
ROC

## Slide 12: Which methods we test
Frequentist on triggering (Frequentist P)
Frequentist on non-triggering (Frequentist N)
ROC Analysis of triggering and non-triggering (max TSS)
TP
TN
FP
FN
Threshold exceeded
Threshold not exceeded
Landslide occurred
Landslide not occured
max TSS = TP/(TP+FN) – FP/(FP+TN)

## Slide 13: Which methods we test
Indeed the other methods have an objective that can be framed in terms of the ROC matrix too
Frequentist P
TPR = TP/(TP+FN) = 5 % (e.g.)
TP
TN
FP
FN
Threshold exceeded
Threshold not exceeded
Landslide occurred
Landslide not occured

## Slide 14: Which methods we test
Indeed the other methods have an objective that can be framed in terms of the ROC matrix too
Frequentist N
FPR = FP/(FP+TN) = 5 % (e.g.)
TP
TN
FP
FN
Threshold exceeded
Threshold not exceeded
Landslide occurred
Landslide not occured

## Slide 15: What we test
Sampling variability
How large is the statistical uncertainty in the estimation of the threshold, due to limited size of the available data set
MSE of threshod parameter
Sample size
Method 1
Method 2
Method 2 is better than method 1
For example:

## Slide 16: What we test
Robustness
Robustness measures how "the outcome of a statistical procedure is affected by the presence of a small number of unusual or incorrect values".
Oxford dictionary of Statistics

## Slide 17: Method
Monte Carlo simulations are used (see Peres and Cancelliere, 2018)
For a given sample size (number of rainfall events) N = 30 repetitions are carried out
For each sample, to test robustness, a separate set with errors is generated:
  p% of the triggering rainfall events are randomly assigned to non-triggering events and vice-versa
  In this way we try to mimic the effect of missing landslide events in inventories, and of rainfall events erroneously being attributed to a landslide (for instance: far rain gauge/landslide triggered by other causes)

## Slide 18: Data
Climate and hydro-geomorphological characteristics of the Peloritani Mountains area (see Peres and Cancelliere, 2018)

## Slide 19: Results: Robustness (p = 10%)
Number of rainfall events = 5’000
These plots show thresholds derived from a “perfect” rainfall-landslide data set vs. a “polluted” data set, where the 10 % of triggering events are exchanged with non-triggering events and vice-versa

## Slide 20: Results: Robustness (p = 10%)
Number of rainfall events = 50’000
These plots show thresholds derived from a “perfect” rainfall-landslide data set vs. a “polluted” data set, where the 10 % of triggering events are exchanged with non-triggering events and vice-versa

## Slide 21: Results: Sampling variability
These plots show the uncertainty in determination of the I-D threshold parameters (intercept and slope), for varying sample-size

## Slide 22: Results: Performance (calibration)
This plot shows the average calibration performance of thresholds with the 3 methods, in terms of the ROC TSS

## Slide 23: Conclusions
Method based on maximization of TSS are the most robust and performing (best trade-off between false positives and false negatives)
At the same time max TSS method has the highest sampling variability
“Frequentist P” method is the least robust and leads to a high number of false positives. Errors in inventories exacerbate this issue
“Frequentist N” method deserves higher attention by the scientific community, as it is more robust, less variable and more performing than widely-used “Frequentist P”
Even if other considerations may constrain the choice of the method, the statistical features illustrated may be useful when taking the decision

## Slide 24: Questions?
Chat with me:
don’t‘ be shy!
Write me a comment