## Slide 1: Airborne Experiment for Soil Moisture Retrieval using GNSS Reflectometry
Authors
Hamza Issa1,2, Georges Stienne1, Serge Reboul1, Maximilian Semmling3, Mohammad Raad4, Ghaleb Faour2 and Jens Wickert3
1 Laboratoire d’Informatique, Signal et Image de la Côte d’Opale (LISIC)
2 National Council of Scientific Research - Lebanon (CNRS-L)
3 German Research Centre for Geosciences (GFZ)
4 Lebanese International University (LIU)

## Slide 2: Outline
Motivation for Soil Moisture Remote Sensing with GNSS-R
GNSS-Reflectometry
General Overview
System Implementation
Conclusion

## Slide 3: Motivation for Soil Moisture Remote Sensing with GNSS-R
GNSS-Reflectometry technique is used for remote sensing in land applications.
This dissertation uses GNSS-R techniques for soil moisture estimation with 1 ms observations.
Introduction
Notes: 1. An increasing number of violent and unpredictable hurricanes and floods have been observed in the last few years all over the world.
2. One of the stages of monitoring floodplains is to measure the river’s levels and currents, as well as the soil moisture, in real time.
3. Comparison of the 𝐶/𝑁_0 between direct and reflected signals allows the estimation of the soil moisture content in the reflective area.

## Slide 4: Motivation for Soil Moisture Remote Sensing with GNSS-R
Scan large surface areas
Quickly reach the areas to monitor.
24 hours detection.
Precisely locate and date the data
Reduced development cost.
GNSS-R Advantages
Introduction
Hard and Impractical

## Slide 5: Outline
Motivation for Soil Moisture Remote Sensing with GNSS-R
GNSS-Reflectometry
    GNSS-R Concept
    GNSS-R Geometry
General Overview
System Implementation
Conclusion

## Slide 6: GNSS-R Concept
Bi-static radar technique
Uses L-band GNSS signals.
Characterize the Earth’s surface.
GNSS-Reflectometry

## Slide 7: GNSS-R Geometry
Surface Type | Active Region
Flat (Smooth) | First Fresnel zone
Rough | Glistening zone
Main Concern
GNSS-Reflectometry

## Slide 8: Outline
Motivation for Soil Moisture Remote Sensing with GNSS-R
GNSS-Reflectometry
General Overview
System Implementation
Conclusion

## Slide 9: General Overview
1. Develop a Geographic Information System to predict the number and the position of the satellites’ footprints over the experimental zones .
2. Develop a system to detect the number and the position of the satellites’ footprints along the real receiver trajectory .
3. Develop GNSS signal processing techniques for airborne reflectometry and assess it on real data.
4. Develop a probabilistic model that links the high rate observation of the in-phase components of the signal with the carrier-to-noise ratio .
5. Link the observations to the soil moisture information of the reflective surface.
6. Link the soil moisture content to each reflective surface
Notes: 1. Develop a Geographic Information System to predict the number and the position of the satellites’ footprints over the experimental zones .
2. Develop a system to detect the number and the position of the satellites’ footprints along the real receiver trajectory .
3. Develop GNSS signal processing techniques for airborne reflectometry and assess it on real data.
4. Develop a probabilistic model that links the 1 ms rate observation of the in-phase components of the signal with the 𝐶/𝑁_0 (SNR) of the signal.
5. Link the 𝐶/𝑁_0 observations to the soil moisture information of the reflective surface.
6. Develop GNSS signal processing techniques for airborne reflectometry and assess it on real data.

## Slide 10: Outline
Motivation for Soil Moisture Remote Sensing with GNSS-R
GNSS-Reflectometry
General Overview
System Implementation
  Detection of the Satellites’ Footprints
    Calculation of the Satellites’ Footprints
    Real Flight Experimentation
  Carrier-to-Noise Ratio: Rate of Observation
Conclusion

## Slide 11: Detection of the Satellites’ Footprints
System Implementation
Drone Sensor (records gyrocopter’s attitude)
Dual Polarization Antenna
Detect the reflective surfaces (footprints) from which each analyzed signal has reflected.
Link the reflected signals to the satellites' footprints.
Real Flight Experimentation
Signal Digitization

## Slide 12: Calculation of the Satellites’ Footprints
Detection of the Satellites’ Footprints
System Implementation

## Slide 13: Coordinates of the specular point S
Calculation of d | Calculation of S (x,y,z)
Calculation of the Satellites’ Footprints
System Implementation

## Slide 14: Coordinates of the First Fresnel Ellipse
Ellipses’ Coordinates | Rotation with angle= -Az | Translation
Transform back to geodetic coordinates for representation on Google Earth.
Calculation of the Satellites’ Footprints
System Implementation

## Slide 15: Real Flight Experimentation
Footprints along the whole receiver trajectory. | Footprints when the receiver was positioned at (
Footprints along the whole receiver trajectory. | 
Detection of the Satellites’ Footprints
System Implementation

## Slide 16: Carrier-to-Noise Ratio: Rate of Observation
GNSS-R uses SNR observations to derive the properties of the reflective surface.
The amplitude of the GNSS signals can’t be directly observed.
For 1 bit quantization, the in-phase component provides a direct observation of the SNR.
High rate SNR observations is needed to cope with the rapid change in the locations of the satellites’ footprints.
System Implementation

## Slide 17: Carrier-to-Noise Ratio: Rate of Observation
Gyrocopter’s parameters during the flight:
Average speed of displacement of the satellites’ footprints during the flight:
Average speed = 26.31 m/sec = 2.63 cm/ms | Average height = 718 m.
Satellite PRN | Average Speed (m/sec) | Average Speed (cm/ms)
1 | 26.42 | 2.64
8 | 26.22 | 2.62
18 | 26.4 | 2.64
32 | 26.13 | 2.61
Very low speed of displacement per ms
Footprints’ localization is in cm accuracy at ms rate
Footprints move approximately 2.63 cm per ms
1 ms rate of observations is applied. (G. Stienne, J. Kucwaj, M. Semmling and S. Reboul, "GNSS signals inversion for amplitude estimation: a concept for high-rate reflectometry," 2018 International Conference on Electromagnetics in Advanced Applications (ICEAA), Cartagena des Indias, 2018, pp. 368-371.)
System Implementation
High speed of displacement per second
The reflective surfaces’ characteristics might change during 1 second

## Slide 18: Outline
Motivation for Soil Moisture Remote Sensing with GNSS-R
GNSS-Reflectometry
General Overview
System Implementation
Conclusion

## Slide 19: Research Novelty
Develop new methods for GNSS-R to deal with the rapid change in the dynamic GNSS receiver's position and the satellites’ footprints.
Develop a Geographic Information System that can predict and detect the number and locations of the satellites’ footprints along a receiver trajectory.
Develop a model to estimate the , from the 1 ms rate observations of the in-phase component of the signals taking into consideration the non linearity of the system.
Usage of the state-of-the-art L5 signals in combination with the traditional L1 signals for estimation.
Conclusion
Notes: So far the LISIC has only applied GNSS-R for static receivers, the first novelty will be to Develop new methods for GNSS-R to deal with the rapid change in the dynamic GNSS receiver's position and the satellites’ footprints
Develop a Geographic Information System that can predict and detect the number and locations of the satellites’ footprints along a receiver trajectory ahead of time .
Develop a new model to estimate the 𝐶/𝑁_0 , from the 1 MS rate observations of the in-phase component of the signals taking into consideration the non linearity of the system.
Usage of the state-of-the-art L5 signals in combination with the traditional L1 signals for 𝐶/𝑁_0 estimation. The L5 signals provide numerous advantages over the L1 and L2 signls like :
Wider bandwidth providing a 10x processing gain.
Improved signal structure for enhanced performance.
Higher transmitted power than L1/L2 signal (~3 dB, or 2x as powerful).
Longer spreading codes (10x longer than C/A).
Enhanced positioning and detection accuracy.
Increased interference rejection and ionospheric correction capabilities.

## Slide 20: Conclusion
GNSS-R technique is an effective tool for remote sensing in land and altimetry applications.
Detection of the satellite’s footprints through the developed software is essential to link the reflective surfaces with the analyzed GNSS signals.
High rate observations (1 ms) is achieved to cope with the rapid displacement of the dynamic GNSS receiver.
The comparison of the between direct and reflected signals allows the estimation of the soil moisture content in the reflective area.
Notes: So far the LISIC has only applied GNSS-R for static receivers, the first novelty will be to Develop new methods for GNSS-R to deal with the rapid change in the dynamic GNSS receiver's position and the satellites’ footprints
Develop a Geographic Information System that can predict and detect the number and locations of the satellites’ footprints along a receiver trajectory ahead of time .
Develop a new model to estimate the 𝐶/𝑁_0 , from the 1 MS rate observations of the in-phase component of the signals taking into consideration the non linearity of the system.
Usage of the state-of-the-art L5 signals in combination with the traditional L1 signals for 𝐶/𝑁_0 estimation. The L5 signals provide numerous advantages over the L1 and L2 signls like :
Wider bandwidth providing a 10x processing gain.
Improved signal structure for enhanced performance.
Higher transmitted power than L1/L2 signal (~3 dB, or 2x as powerful).
Longer spreading codes (10x longer than C/A).
Enhanced positioning and detection accuracy.
Increased interference rejection and ionospheric correction capabilities.

## Slide 21: Special Thanks
A special thanks goes to the MARCO Project which provided this research with the drone, essential to the global implementation of this research.
Notes: So far the LISIC has only applied GNSS-R for static receivers, the first novelty will be to Develop new methods for GNSS-R to deal with the rapid change in the dynamic GNSS receiver's position and the satellites’ footprints
Develop a Geographic Information System that can predict and detect the number and locations of the satellites’ footprints along a receiver trajectory ahead of time .
Develop a new model to estimate the 𝐶/𝑁_0 , from the 1 MS rate observations of the in-phase component of the signals taking into consideration the non linearity of the system.
Usage of the state-of-the-art L5 signals in combination with the traditional L1 signals for 𝐶/𝑁_0 estimation. The L5 signals provide numerous advantages over the L1 and L2 signls like :
Wider bandwidth providing a 10x processing gain.
Improved signal structure for enhanced performance.
Higher transmitted power than L1/L2 signal (~3 dB, or 2x as powerful).
Longer spreading codes (10x longer than C/A).
Enhanced positioning and detection accuracy.
Increased interference rejection and ionospheric correction capabilities.

## Slide 22
THANK YOU
FOR YOUR ATTENTION

## Slide 23: Questions?