## Slide 1: EGU 2020
A new automated radiolarian image acquisition, processing and identification workflow
Martin Tetard1, Ross Marchant1,2, Giuseppe Cortese3, Yves Gally1, Thibault de Garidel Thoron1, Luc Beaufort1.
1 Aix Marseille Univ, CNRS, IRD, Coll France, INRAE, CEREGE, Aix-en-Provence, France.
2 School of Electrical Engineering and Robotics, Queensland University of Technology, Brisbane, Australia
3 GNS Science, Lower Hutt, New Zealand.

## Slide 2
« Recent technological advances in image acquisition, processing, and recognition now enable automated procedures, from microscopic slide field-of-view acquisition to taxonomic identification. »
Step 1: slide preparation
Just a reminder
Marine planktic micro-organisms,
Siliceous shell,
50-500 µm,
Known since the Cambrian (540 Ma),
Presence / Absence, abundance of some species are used as tracers,
Very useful for productivity and temperature reconstructions, for tracking water masses, and for biostratigraphical studies.
However, their investigation requires:
a significant taxonomical knowledge (identification can be biased between operators),
time, as about 300 specimens per sample need to be counted for reliable analyses.

## Slide 3
Step 2: image acquisition
Step 1: slide preparation
Original protocol for radiolarian slides preparation.
Main issues:
-Lots of loss,
-Large cover slides.
3D printed decanter for random settling of particles on cover slides.
3D printed slide guide for mounting cover slides.
Diagram of the cover-slip holder placed on a stand into a beaker = 1 sample per system (Lazarus, 1994).
New protocol for slide preparation.
Advantages:
-Minimise the loss of material,
-very fast tu use and clean,
-1 sample per tank = 8 samples per system (and per slide).
Cross-section of a tank.
A new random settling protocol

## Slide 4
Step 2: image acquisition
1 FOV = hyperfocus of 15 images acquired by incrementally stepping through the slide (step size: 10 µm).
1 slide = 8 cover slides (= 8 samples, after Beaufort et al. (2014) ),
1 sample = 324 fields of view (FOVs).
A new automated acquisition
www.microbehunter.com

## Slide 5
Step 3: image stacking

## Slide 6
Step 4: image processing and segmentation
Step 3: image stacking
For each FOV, the 15 mages are then automatically stacked using a depth map on Helicon Focus, The focally stacked FOV is saved send for image processing.
A new automated FOVs stacking
Stack of 15 original FOVs
Stacked FOV

## Slide 7
Step 4: image processing and segmentation
  Automated image processing, segmentation, and vignettes export.
A new automated segmentation
1 sample = ~ 2000 - 3000 vignettes,
1 slide = ~ 20000 vignettes.
Stacked FOV
Defining ROIs
Applying ROIs on inversed stacked FOV
Vignette for each specimen

## Slide 8
Step 5: image recognition
Few examples of radiolarian specimens after the automated image processing and segmentation. Scale bars 100 µm
A new automated segmentation
Anthocyrtidium ophirense
Botryostrobus auritus-australis
Didymocyrtis tetrathalamus tetrathalamus

## Slide 9
Step 5: image recognition
« Convolutional Neural Networks (CNNs) enable Deep Learning approaches for classifying images of different microfossil taxa. »
A new automated recognition
Particle_trieur, a software developed at CEREGE (Marchant et al., 2020) is used to built a database and classify each image.

## Slide 10
Step 6: Image storage and census counts
« Convolutional Neural Networks (CNNs) enable Deep Learning approaches for classifying images of different microfossil taxa. »
Database
Currently 17.065 images, recovered from West Pacific Warm Pool samples,
112 classes in total, 84 trained classes (as classes with less than 10 images are fused into a single one),
Overall accuracy of 90 %.
Confusion matrix for the trained CNN (based on resnet50).
Example of recognition scores for a few radiolarian classes.

## Slide 11
Step 6: Image storage and census counts
Automated counts and image storage
The trained CNN automatically returns images identification.
3 kinds of results are automatically exported:
(1) Identified individual images are saved into folder corresponding to their assigned classes and samples.
(2) Census data and (3) morphometric measurements are also automatically saved for each sample and core.

## Slide 12
Operational workflow
https://www.youtube.com/watch?v=4U66wgLoVPg&feature=emb_title

## Slide 13
Accuracy of the CNN on random samples
In average:
98 % of radiolarian images were actually recognised as radiolarians (a),
90 % of radiolarians were identified as the correct radiolarian taxa (b),
99 % of the non-radiolarian images were recognised as non-radiolarian (c),
98 % non-radiolarian images were assigned to the correct class (d),
4 % were radiolarian false positives (non-radiolarian images among radiolarians, e),
0.3 % were non-radiolarian false positives (radiolarian images among rnon-adiolarians, f).
8 new random samples (10.288 images) from the WPWP were prepared, and processed according to the described protocol.
Vignettes were automatically identified and manually checked to test the accuracy of this new recognition workflow.

## Slide 14
Conclusion
A new automated radiolarian workflow was developed and consists of a sequence of 6 steps:
1: A new microscopic slide preparation protocol that decreases the loss of material,
2: Automated microscope image acquisition of slides bearing up to 8 samples at different focal depths,
3: Automated stacking of each batch of fields of view (FOV) images,
4: Automated FOV image processing and segmentation to generate individual images for every radiolarian specimen,
5: Automated radiolarian recognition using a CNN,
6: Automated export of census data and morphometric measurements per sample, and storage of radiolarian images.
Autoradio database
https://autoradiodatabase.wordpress.com/database/