## Slide 1: Retrieving tropospheric parameters using predicted multi-GNSS orbits and clocks
Zhiguo Deng1,3, Florian Zus1, Kyriakos Balidakis1, Jens Wickert1,2 and Harald Schuh1,2,3
deng@gfz-potsdam.de
(1) GFZ Potsdam, Germany
(2) Technical University Berlin, Germany
(3) GeoBM GmbH, Germany

## Slide 2: Content
Rapid and ultra-rapid multi-GNSS products: GBM & GBU
Orbit & Clock prediction method
Validation of Orbit & Clock prediction
ZTD from predicted Orbit and Clock
Conclusion and Outlook

## Slide 3
Rapid and ultra-rapid SP3: GBM & GBU
Product includes:
5 min. orbit & 30 sec. clock
Daily ERP parameters
Daily ISB for MGEX stations
Up to 129 satellites
Satellite system | Observation types
GPS | L1/L2
GLONASS | L1/L2
Galileo | E1/E5a
BeiDou II | B1/B2
BeiDou II+III | B1/B3
QZSS | L1/L2
Start GBU
Start GBM
(Up to 28 satellites of BDS III are added at the end of 2019.)

## Slide 4
Multi-GNSS network for rapid & ultra rapid
Rapid
Ultra rapid
(02-May-2020)

## Slide 5
GBU (09:00 job, 3 hours prediction part 12:00~15:00) vs. GBM
GBU Orbit prediction
24 h SP3
48h
24 h SP3__________
24 h SP3
GBM
GBU
Sys. | T [cm] | N [cm] | R [cm]
G | 3.4 | 3.0 | 0.6
R | 6.0 | 5.1 | 1.4
E | 5.0 | 4.0 | 1.2
C(MEO) | 9.0 | 6.6 | 2.3
C(IGSO) | 23.8 | 14.8 | 7.5
C(GEO) | 373.5 | 117.5 | 39.9
J | 140.0 | 53.8 | 33.8

## Slide 6
GBU Clock prediction
24 h ORB
24 h ORB
24 h Clock
24h
24 h Clock
Correct clock using orbit fitting residuals before clock prediction.
The quality of predicted orbit & clock is analysed with SISRE (Signal-In-Space Range Error):

## Slide 7
SISRE validation
24 h calculated
24h predicted
24 h caculated
GBM
3 hours predicted SP3 vs. GBM
 | G | R | E | C | J
RMS[m] | 0.11 | 0.30 | 0.04 | 0.41 | 0.33
STD[m] | 0.04 | 0.11 | 0.01 | 0.07 | 0.15
After removing a clock bias over 3 hours for each satellite.

## Slide 8
ZTD from predicted SP3
24 h
24 h
GBU SP3
Calculated part Predicted part
24 h observation
24 hours static PPP
24 h ZTD
24 hours ZTD product
In the predicted part only the satellites with STD(SISRE) < 2.5 cm are used. Clock bias can be absorbed by ambiguity.
Compare the last 2 hours ZTD product with:
Parameters: 30 min. ZTD, 24 h. gradients and coordinates, receiver clock error.
1) ZTD from PPP using GBM SP3
2) ZTD from NWM (numeric weather model)

## Slide 9
ZTD (predicted SP3) vs. ZTD (GBM SP3)
ZTDs from 146 stations (DOY 332-362 in 2019) are analyzed. The color indicates the RMS deviation for each station.
The histogram of ZTD differences shows a mean of 1.2 mm and a STD of 13.8 mm. (outlier>100mm)
mm

## Slide 10
ZTD (predicted SP3) vs. NWM
The comparison with the weather model shows an average RMS deviation of about 13 mm.
NWM data comes from the atmospheric reanalysis
ERA5 (ECMWF)
Stations where RMS deviation exceeds 40 mm are removed from statistic (outliers)
Stations are sorted with respect to the latitude

## Slide 11: Conclusion and Outlook
The GNSS orbit and clock determination and prediction benefits from the more stable clock.
SISRE for Galileo is the lowest.
ZTDs from 140 global stations using good* predicted satellite orbit and clocks are validated with a reference solution and a NWM. RMS deviations are about 13 mm.
ZTDs estimated from predicted orbit and clock products are sufficiently accurate for time critical meteorological applications.

## Slide 12: Thank you for your attention