## Slide 1: Estimating regional-scale fresh-brackish-salt groundwater distributions: challenges and recent advancements
Marc F. P. Bierkens, Jude King, Joeri van Engelen, Jarno Verkaik, Daniel Zamrsky, Gu Oude Essink

## Slide 2: Deltas and coasts under threat

## Slide 3: Threats to coastal and delta fresh groundwater resources
-
+/-
Population and economic growth
Climate change
Groundwater pumping
Sea-level rise
Surface sealing
Irrigated agriculture
Urbanisation
Recharge
Groundwater decline Saline groundwater upconing Salt groundwater intrusion
Land subsidence
+
+
+
+
+
+
-
+/-
+
+
+
The complex cause-effect chain of global change and coastal groundwater resources
-

## Slide 4: Obtaining current fresh-brackish-salt water coasts and deltas
Important for:
Exploring possible sources of fresh and brackish water (offshore and onshore): (sustainably) extractable fresh groundwater?
Future projections: sea-level rise, climate change, socio-economic change: (sustainably) extractable fresh groundwater?
How to obtain:
Observations
Density-dependent groundwater modelling

## Slide 5: Observations: airborne EM
www.bgr.bund.de
= EC Water
+lithology (formation factor)
Flight lines
Bulk EC
PhD Thesis Jude King

## Slide 6: Observations; airborne EM: synthetic survey experiment
Existing data used to simulate AEM survey
FreshEM salinity(B) and GeoTOP lithology (C) combined to create bulk EC (D).
Simulated airborne acquisition and drillings (undertaken at different densities (distance flightiness and drillings).
90 combinations of inverted Bulk EC and lithology (formation factors)
90 estimated of chloride concentration (150 million cell synthetic model tested).
Results compared with synthetic model (“truth”) to highlight optimal configurations
King et al., ERL (2020)

## Slide 7: Observations; airborne EM: synthetic survey experiment
~€200k
€
Accuracy
~€650k
€
Careful use of inversion model and reducing flightline spacing shows greatest improvement
Lithology not that important with high salinity contrasts!
Mean Absolute Error (MAE) of different flightline spacing and lithological information as vertical metres drilled/km
King et al., ERL (2020)

## Slide 8: Modelling the fresh-salt-brackish groundwater distribution
A model experiment
Homogenous Hydrogeology Fixed boundary conditions: start fully salt and let it freshen up with fixed recharge and with boundary at current sea-level | Heterogenous Hydrogeology Fixed boundary conditions: start fully salt and let it freshen up with fixed recharge and with boundary at current sea-level
Homogenous Hydrogeology Variable boundary conditions: start fully salt and let it freshen up with fixed recharge. Next simulate a full glacial cycle for sea-level; recharge constant | Heterogenous Hydrogeology Variable boundary conditions: start fully salt and let it freshen up with fixed recharge. Next simulate a full glacial cycle for sea-level; recharge constant
So:
Palaeo-modelling is necessary.
Sharp interface models cannot be used.

## Slide 9: Modelling: global coast; unconsolidated deposits
Thickness and hydrogeological makeup of coastal aquifers -> Coastal typology (subsidence rate, sediment flux, sand/mud ratio)
PhD thesis Daniel Zamrsky
124 models for each for each COSCAT region
Parallel SEAWAT
100 m horizontal and 10 m vertical 103-104 cells

## Slide 10: Modelling: global coast; unconsolidated deposits
This study:
5.1 km3/km
Post et al. (2013):
6.3 km3/km
This study:
7.5 km3/km
Post et al. (2013):
4.8 km3/km
Zamrsky et al., Frontiers in Earth Science (2020)

## Slide 11: Modelling: Nile delta
PhD project Joeri van Engelen
Deltas
8000 BP
7500-6000 BP
~70 km
Map/Nile
1 km horizontal and 20 m vertical ~1 million cells
Parallel SEAWAT
Van Engelen et al. HESS (2020).

## Slide 12: Modelling: All deltas (sensitivity analysis with 240 3D-models)
PhD project Joeri van Engelen
Deltas
Offshore fresh groundwater
Onshore saline groundwater
Van Engelen et al. (under review)

## Slide 13: Conclusions
Estimating fresh-brackish-salt water in coasts and deltas:
Airborne EM: good prospects but relatively expensive compared to modelling
  Suitable for detailed regional-scale studies
  In case of salinity contrasts: lithology less important
  Can be used as initial conditions for modelling -> used in calibration and effect studies
Density-dependent groundwater flow modelling
  Suitable for regional to supra-regional scales and including offshore resources
  In case of heterogeneity: needs palaeo-modelling and can’t use sharp interface approximations.
  New codes (parallel SEAWAT) allows for very large models and long integration times
  Global-scale analyses are slowly becoming within reach

## Slide 14: Thank you!
: m.f.p.bierkens@uu.nl
www.globalhydrology.nl
: @waterbier

## Slide 15: Numerical issues regarding modelling
Coastal modelling
100 m hor., 10 m vert., 103-104 active cells
Time steps: 10-100 years (flow); adaptable (transport)
Integration time: 250,000 years
Longitudinal dispersivity: 1 m
Solver: FD (advection and dispersion)
Average runtime per run: 12hrs-20 days
10 COSCAT regions with 124 runs per region
1 core per run
Delta modelling
1000 m hor., 20 m vert., 106 active cells
Time steps: adaptable (transport)
Integration time: 30,000 years
Longitudinal dispersivity: 2 m
Solver: TVD (advection) FD (dispersion)
Average runtime per run: 4 days
48 cores on 2 nodes per run

## Slide 16: Numerical issues regarding modelling
Stability criteria
Peclet number criterium: cell size < 2-10 times longitudinal dispersivity: not relevant for the solvers used in SEAWAT where advection and dispersion are solved separately.
Three criteria that are relevant:
  Courant number for advection part (use of variable time step)
  Neuman criterium for dispersion part (use of variable time step)
  Source/sink criterium: extraction rate times time step < water volume in cell