## Slide 1
Using automatic hydrograph separation approach to widen the amount of river runoff
characteristics for water regime transformation analysis
Lomonosov Moscow state university, Faculty of Geography, Hydrology Department
Water Problems Institute, Russian Academy of Science
MAIN GOAL: to estimate contribution of different nourishment sources and phases of water regime to river hydrograph formation and maximum runoff in particular
OBJECTIVES:
To investigate different hydrograph separation methods for the plain rivers on European part of Russia
To create a universal algorithm, based on graph analytics and complex hydro-meteorological analyses
To verify the separation algorithm for 35 watersheds and to analyze changes of main hydrological parameters in recent hydro climate conditions
Principal scheme of hydrograph separation
1
2
Created algorithm of automatic hydrograph separation (GrWat)
by Ekaterina Rets, Maria Kireeva and Timofey Samsonov
Decrease in Seasonal flood volume and increase in occasional flood volume
In recent hydro climate conditions it is very difficult to create universal algorithm for hydrograph separation
Drops in the rate of maximum annual discharge to maximum discharge during winter
Increase in duration of the deficit period
Increase in number of the flood waves
Obvious hydrograph transformation
Visualization of the results: .html report file
3
Principal scheme of GrWat algorithm with 3 main blocks
Conclusions
4
Intra annual and long-term changes of main hydrological parameters
Seasonal flood wave
Basically for all station volume of seasonal flood decreased as well as snow melt maximum
5
DATA:
Daily discharge for 55 representative watersheds for 1945 - 2017
Daily NOAA-CIRES 20th Century Reanalysis V2 (1945-1978) and ERA-Interim Reanalysis data for temperature and precipitation
Similar algorithms, realized in international practice (software: BFI+, FlowComp, WHAT, RC)
Main blocks Main groups of calibrated parameters
Separation of thaw peaks overlapped on the main seasonal-flood wave
Chart: Q, m3/s
The use of the reanalyze data to identify rain and snow melt peaks
Assumed mechanisms
Zero ground water input during the day of the Q max
Linear interpolation of ground water discharge from start to the
end of seasonal flood wave
Well-pronounced seasonal flood wave (> 50 % of the runoff)
Uncertain form of seasonal flood wave with overlapping rain
Stable summer-autumn low flow period
Autumn occasional flood period
Well-pronounced seasonal flood wave
Stable summer-autumn low flow period
Autumn occasional flood period
Melt water
Rain water
Ground water
East-European type of water regime and
hydrograph separation according to Kudelin (1973)
Snow melt
> 50 %
Rain
<20 %
ground
<20 %
Theoretical approach
1-4: different types of connection between surface water and ground water layers
(Kudelin, 1967)
Thaw floods during cold period
Thaw floods overlapping on main seasonal flood wave
Rain floods during warm period
Assumed classification of occasional floods:
Rain floods overlapping on main seasonal flood wave
4 main chapters in .html report file (example for riv.Vetluga – station Vetluga)
Medveditsa – Archedinskaya (South part of study area)
Oka – Murom (Central part of study area)
North Dvina – Ust-Pinega (North part of study area)
Volume of seasonal flood Maximum discharge of seasonal flood
Volume of seasonal flood Maximum discharge of seasonal flood
Volume of seasonal flood Maximum discharge of seasonal flood
Seasonal flood wave
Annual volume of rain occasional flood s Date of maximum discharge of rain occasional floods
Mezen (North) б) Oka (Central)
в) Khoper (South) г) Samara (East)
Volume all of occasional rain floods rise mostly and the dates of rain flood maximum in last 40 years have tendency to observed in all seasons. Number of thaw floods rise as well as their dates switch to later period
Number of thaw occasional floods Date of maximum discharge of thaw occasional floods
The study has been carried out with the support of the Russian Science Foundation [Project No. 19-77-10032]
The study has been carried out with the support of the Russian Science Foundation [Project No. 19-77-10032]