## Slide 1
Air-sea fluxes following the unusual summer ice retreats measured by saildrones
Dongxiao Zhang (JISAO/University of Washington and NOAA/PMEL)
Chidong Zhang (NOAA/PMEL)
J. Cross, C. Mordy, E. Cokelet, C. Gentemann, A. Chiodi, P. Stabeno, R. Jenkins, C. Meinig, N. Lawrence-Slavas, H. Tabisola, M. Wang

## Slide 2: Motivation 1) Vast ocean area normally covered by sea ice opens up for air-sea interaction, which will energize weather system development; 2) Observe air-sea interaction in newly opened Arctic to establish a baseline dataset and to provide real time data for improving forecasts; 3) Demonstrate the feasibility of using autonomous platforms for sustained observation.
Ice edge 15%: Summer ice retreats further North
Sept. 1982
Sept. 2019
Ice concentration (%)
NOAA OI Ice Concentration along 168oW
Notes: Add sensors to

## Slide 3
TECHNOLOGY OVERVIEW
SAILDRONE
Unoccupied surface vehicle (USV)
Green Tech.: Wind propulsion; Solar power electronics.
Long Endurance: 12-month; 16,100 km.
Large Payload: >100 kg; Large number of sensor packages.
7.5 m / 23 ft long
5 m / 15 ft tall
wind power for
propulsion
solar power
for electronics
satellite link
for live data
human scale

## Slide 4: Saildrones: Global Class Autonomous Surface Vehicles for Air-Sea Interaction Observation
CRADA PMEL-Saildrone Inc 2014
Bering Sea summer 2015 2016 (surface MetOcean, acoustic fish biomass)
Tropical Pacific Observing System (TPOS) and NOAA Tech. Development 2016-2019 (Air-sea heat, momentum and CO2 fluxes, ADCP upper ocean currents)
Fast development, production and application cycle, Public-Private Partnership.
Meinig et al. 2019 OceanObs’19

## Slide 5: Autonomous Surface Vessels as Low-Cost TPOS Platforms for Observing the Planetary Boundary Layer and Surface Biogeochemistry Co-PIs: M. Cronin, D. Zhang, A. Sutton, C. Meinig Postdoc: Samantha Wills
Testing the ability of Saildrone to make
climate-quality measurements in the Tropics
Three 6-month missions:
1) NASA salinity study (SPURS II) and 125°W section (Sept.2017)
2) Equatorial sections 140°W, with and against currents (Oct. 2018)
3) Cluster of 4 drones, adaptive sampling around 140°W (June 2019)

TAO buoy with CO2 flux sensors
NASA SPURS II Study Site
TAO buoys
Legend:
Saildrone Mission #1
Saildrone Mission #2
Saildrone Mission #3
Notes: Add sensors to

## Slide 6
Off-the-shelf Sensors (data put on GTS):
  Air Temperature and Relative Humidity
  Air Pressure
  SST (@0.6m)
Wind and Wind Stress (Bulk and covariance)
ADCP currents (upper 100m) or Echosounder fish biomass
Air-sea heat fluxes (LW and SW radiation, bulk latent heat and sensible heat)
Waves (significant wave height and period)
Cameras (ice and cloud images)
BGC Suite
  Air pCO2, Sea surface pCO2 and pH
  Dissolved Oxygen
  Chla, CDOM, Red Backscatter
Sunlight & IR
15 Sensor Packages 22 Essential Variables

## Slide 7
Saildrone tracks around SPURS2 WHOI buoy
Zhang et al. 2019
within 12-km

## Slide 8
2019 Joint Mission for Observing Arctic Sea Ice Environment
PMEL, UW/JISAO, Farallon Inst., UW/APL, and Saildrone, Inc.
5 Sailed through narrow Bering Strait Reaching the Melting Ice Edge
Unescorted, Remotely Controlled 1000s km Away
Chidong Zhang et al.
HYCOM SST forecast HYCOM ocean current forecast
6 Saildrones launched from Dutch Harbor
1 Stayed in Bering Sea to follow tagged seals and have fish biomass survey

## Slide 9
2019 Joint Mission for Observing Arctic Sea Ice Environment
PMEL, UW/JISAO, Farallon Inst., UW/APL, and Saildrone, Inc.
5 Sailed through narrow Bering Strait Reaching the Melting Ice Edge
Unescorted, Remotely Controlled 1000s km Away
Chidong Zhang et al.
Baby seal takes a ride HYCOM ocean current forecast
6 Saildrones launched from Dutch Harbor
1 Stayed in Bering Sea to follow tagged seals and fish biomass survey

## Slide 10
Fast melting opened Bering Strait quickly
5 Saildrones through BS by June 4
1st ice encounter June 14
Sampled in and near bands of floating ice and followed a profiling float June 16-26
Really rapid retreat of sea ice in July
Saildrone spent much of August north of 75oN close to and in Marginal Ice Zone
7-day Saildrone Tracks over GHRSST and Ice Edge
observation vs. ECMWF reanalysis

## Slide 11
Ice pictures by Saildrone 1035, June 14, 2019
Ice pictures by Saildrone 1035, June 21, 2019
Saildrone tracks on HYCOM SST prediction

## Slide 12
Observation SD 1035 vs. ERA5 reanalysis (June 2019)
Bias=ERA5-Observation
Cor.=0.86, RMSE=1.1m/s, Bias=-0.31m/s
Cor.=0.78, RMSE=0.5 0g/kg, Bias=-0.28 g/kg
Cor.=0.67, RMSE=1.7oC, Bias=-0.63oC
Cor.=-0.03, RMSE=2.3oC, Bias=-0.95oC
Cor.=0.49, RMSE=25.1W/m2, Bias=-3.7W/m2
Cor.=0.9, RMSE=76W/m2, Bias=2.4W/m2

## Slide 13
Cor.=0.73, RMSE=20.1W/m2, Bias=-2.3W/m2
Observation SD 1035 - ERA5 reanalysis (May – Sept. 2019)
Bias=ERA5-Observation
Cor.=0.93, RMSE=1.06m/s, Bias=-0.27m/s
Cor.=0.91, RMSE=0.44 0g/kg, Bias=-0.26 g/kg
Cor.=0.88, RMSE=1.24oC, Bias=-0.25oC
Cor.=0.8, RMSE=1.51oC, Bias=-0.61oC
Cor.=0.9, RMSE=74.8W/m2, Bias=6.5W/m2

## Slide 14: Conclusion
Reliable, long-range, long-endurance, GREEN autonomous ocean observing platforms, adaptive to rapidly changing environment, ice retreating/advancing, fronts, eddies, HABs ...
Capable of making measurements of 22 Essential Ocean and Atmospheric Variables, including air-sea heat, momentum, CO2 fluxes, and upper ocean currents, critical for understanding air-sea interaction processes.
Saildrones have proven to be
Future Work (transition to operation)
Test and Improve strategies in navigating and target-sampling complex ocean and atmospheric environments and processes.
Evaluate the benefits of saildrone data (high frequency simultaneous ocean and atmospheric measurements, crossing fronts, adaptive) to Numerical Weather Prediction (NWP) and ocean prediction models.
Ice Fraction
May 1. 2019
Sept 1. 2019
Latent and Sensible
Heat Flux (W/m2)
3. Valuable for evaluating and feeding real-time data to operational numerical forecasting models.

## Slide 15
Thanks!