## Slide 1
Paola Bacigaluppi*, Robert M. Boes, David F. Vetsch
Tsunami modelling on lake scales - a sensitivity analysis
D1899 | EGU2020-20733
6th May 2020
Contact: bacigaluppi@vaw.baug.ethz.ch
Affiliation: ETH Zurich, Laboratory of Hydraulics, Hydrology and Glaciology (VAW)
© Authors. All rights reserved
Picture @ A. Shynkarenko

## Slide 2: Motivation: Lake Tsunamis
Goal: Understand governing mechanisms of genesis, propagation and inundation of tsunamis in lakes.
Tsunamis may occur in every acquatic system
Hystorically:
563 AD Lake Geneva: - rockfall-induced delta-collapse
- modelled wave heights up to 8m
1601 AD Lake Lucerne: - earthquake-triggered sublacustrine slope failure
& rockfall in Bürgenstock
- wave heights of 4m in Lucerne
1941 AD Laguna Palcacocha, Peru: - large avalanche
- killing ~ 1,800 to 7,000 inhabitants
climate warming tends to enhance slope instabilities
Urge for prediction of possible hazardous events
To know more check:
D1900 |
EGU2020-4711
Picture @ K. Kremer

## Slide 3
3
Main key questions: Overview
Wave generation processes
Propagation of waves
Inundation
Proof of concept – Workflow
BASEMENT A freeware simulation tool for hydro- and morphodynamic modelling
Impact on the shoreline
Trigger mechanismus
Key Properties: Lake Tsunami Modeling
Efficient Simulation Workflow

## Slide 4: Goals of the present contribution
Focus on propagation & inundation:
Sensitivity analysis on lake scales for diverse modelling equations & softwares
Goal:
Understand governing mechanisms of genesis, propagation and inundation of tsunamis in lakes.
Tsnamis: long waves compared to water depth for submerged landslides
What mathematical model fits best?
Depends on the scales of the physical problem – e.g. relative wave length
Presence of linear or non-linear waves for lake scales
Shallow Water model: no frequency dispersion ( ~ propagation time & shape of wave)
Frequency dispersion: Boussinesq-type model
<
h : water depth
qx : discharge, x
g : grav. acceleration
Sh: lateral i/o discharge
Sfx: friction, x
zB : bottom elevation

## Slide 5
5
Depth-averaged 2D models based on the Shallow Water equations
Accurate prediction of shoaling
No intrinsic dissipation mechanism
Boussinesq-type equations derived from Schäffer and Madsen (1995)
and
Good for broken waves (shocks)
Simple and efficient for run-up
Legend:
𝜂(x,t) : wave shape
A : wave amplitude
h : water column height
href : still water reference height
qx : discharge, x
g : grav. acceleration
Sh : lateral i/o discharge
Sfx : friction, x
zB : bottom elevation
Propagation of waves & mathematical model

## Slide 6
6
Depth-averaged 2D models based on the Shallow Water equations
Boussinesq-type equations derived from Schäffer and Madsen (1995)
and
Propagation of waves and what to consider – Insight on lake scales
 | BASEMENT v3 | BoussClaw (GeoClaw 5.6)
Under developement since | 2003 | 1994
Purpose of use | Teaching, research & projects | Teaching, research
Hyperbolic systems of PDE | Shallow Water Eqs. | Boussinesq-type Eqs.
Simulated dimensions | 1- & 2-D | 1- & 2-D
Numerical Approach | Finite Volumes | Finite Volumes
Computational Mesh | Unstructured | Structured
Multi-core CPU simulations |  | 
Support of GPGPU accelation |  | 
Typical scales of Lakes (cf. Lake Lucerne)
s = [800, 1600, 3200, 6400]m,
href = [40, 80, 120, 160, 200]m and,
Generated wave amplitudes A=[0.1,0.2,0.3, 0.4, 1, 2, 4, 6]m.
Relative wave height Ɛ=A/href between 0.0005 – 0.15
Wave length Lw between 749 – 64892 m
Ratio (A+href)/Lw between 0.0031 – 0.061
Legend:
𝜂(x,t) : wave shape
A : wave amplitude
h : water column height
href : still water reference height
s : propagation distance with constant bathymetry
𝛽 : slope angle for the run-up shoreline
Outlook
Difference between Basement and BoussClaw for Gauge 4
< +0.06%

## Slide 7
7
Preview of BASEMENT v3.0 performance abilities – Lake Lucerne
Simulation – fine grid (video)
Case Study
Water surface: 434m a.s.l. [Source: https://www.hydrodaten.admin.ch/de/2207.html]
Initial conditions:
Two submerged landslides
– Δ= - 5m (c.f. Figure below, area with light blue dot)
– Δ= - 7m (c.f. Figure below, area with yellow dot)
Simulated time since landslides: 160s
Time needed for simulation, 2.6million cells
Area of a single cell: 50m2
Case Study
GPU: 103.3s

## Slide 8
8
Conclusions and Outlook
BASEMENT 3.0 for tsunami modelling
Non-linear Shallow Water Equations appear suitable for the considered lake scales
Qualitative proof of concept of wave generation, propagation & run-up on selected case study of Lake Lucerne
Conclusions
Outlook
What controls wave propagation in narrow and confined lake basins?
Can the simulations be matched with hydraulic laboratory modeling & historic event description?
Acknowledgments
This project is financed by the Sinergia Project of the Swiss National Science Foundation nr. 171017.