## Slide 1: Determination of thermal conductivities in the laboratory and the field: A comparison
Linda Schindler, Sascha Wilke, Simon Schüppler, Hanne Karrer, Roman Zorn, Hagen Steger, Philipp Blum

## Slide 2: Agenda
Geographical and geological setting
Test site - Drilling profile
Lab characterization
  Petrophysical measurements
  Comparison of thermal conductivity and other rock parameters
Thermal Response Test
Comparison of the thermal conductivity measured in the lab and the field
Conclusion

## Slide 3: 1. Geographical position and geology
Source: googlemaps.com
Test site in the Northern Black Forrest in South West Germany (~ 45 km western of Stuttgart)
100 m deep drilling into the Upper and Middle Buntsandstein
Installation of borehole heat exchanger (double U-pipe)

## Slide 4: 2. Test site – Drilling profile
Cross bedding
Heterogeneous layer
Installation of borehole heat exchanger

## Slide 5: 3. Lab characterization – Determination of petrophysical properties
Thermal conductivity
Porosity, density
Permeability
Grain size
Grain density
Mineralogy

## Slide 6: 3. Lab characterization – Density
Mineral | Density [g/cm³]
Quartz | 2.65
Feldspar | 2.56-2.76
Mica | 2.80-3.20
Hematite | 4.15
Ilmenite | 4.50-5.00
Calcite | 2.70
Source: Matthes, S. (2001) Mineralogie, Springer Verlag, Berlin.
Chart: Matrix density [g/cm³]
| <2.65 | 2.65-2.70 | 2.70-2.75 | 2.75-2.80 | 2.80-2.85
 | 5 | 105 | 33 | 7 | 1
Chart: Matrix density [g/cm³]
| <2.65 | 2.65-2.70 | 2.70-2.75 | 2.75-2.80 | 2.80-2.85
 | 5 | 105 | 33 | 7 | 1
Mineralogy:
Quartz
Feldspar (Mikrokline)
Mica (Biotite & Muskovite)
Hematite
Rutile
Illite

## Slide 7: 3. Lab characterization – Porosity & permeability
Low permeability
Chart: Porosity [%]
| < 5 | 5 - 10 | 10 - 15 | 15 - 20 | 20 - 25 | > 25
 | 0 | 25 | 85 | 43 | 2 | 0
Fractures
Fractures
Fractures
Fractures
Fractures
Chart: kf [m/s]

## Slide 8: 3. Lab characterization – Thermal conductivity
Slight anisotropy due to:
  Layering
  Clay lenses
λWater= 0.6 W/mK
λAir = 0.026 W/mK
Positive correlation of λ and saturation grade apparent

## Slide 9: 3. Lab characterization – Thermal conductivity vs. density
No correlation between λ and density apparent
Potential reason: Heterogeneity of the sandstone
Mineral | λ [W/mK]
Quartz | 1.36-12.00
Feldspar | 2.11
Biotite | 1.70-2.30
Muskovite | 0.84-5.10
Hematite | 11.20
Clay minerals | 2.90
Calcite | 3.20-5.50
Rutile | 5.12

## Slide 10: 3. Lab characterization – Thermal conductivity vs. porosity
Negative correlation of λ and porosity apparent

## Slide 11: 3. Lab characterization – Thermal conductivity vs. grain size and porosity
Classification of sandstone depending on grain size
Negative correlation of λ and grain size visible

## Slide 12: 4. Field characterization – Classical TRT
TRT October 2017  Convergence was not achieved
TRT November 2018
Analysis according to German Standard VDI 4640-Blatt 5 assuming an infinite line source:
 | Duration [days] | q [W/m]
TRT 2017 | 6 | 50
TRT 2018 | 12 | 64.4
Tf: Fluid temperature [°C]
q: Heat injection rate per unit length [W/m]
λ: Thermal conductivity [W/mK]

## Slide 13: 4. Field characterization – Thermal conductivity
Chart: λ [W/mK]
Chart: λ (W/mK)
Fractures
Fractures
Fractures
Fractures
Fractures
71 m
Vertical ground water flow?

## Slide 14: 5. Comparison of thermal conductivity determined in the lab and the field
At shallow depth: Poor match of λ determined in the lab and the field
  Potential reason: clay rich layers
λdry ≈ 2.46 W/mK λsaturated ≈ 4.22 W/mK λTRT 2018 ≈ 4.58 W/mK
Chart: λ [W/mK]

## Slide 15: 6. Conclusion
Thermal conductivities of a sandstone are correlated with other petrophysical parameters;
Thermal conductivities are spatially resolved along a 100 m drill core.
Thermal conductivity is anisotropic.
In contrast to previous studies no clear correlation between thermal conductivity and porosity could be detected;
Determined thermal conductivities in the field are higher than in the laboratory.
Density
Porosity
Saturation grade
Grain size
Correlation degree to λ

## Slide 16: Thank you for your attention!
Linda Schindler
Emmy-Noether-Str. 11
76131 Karlsruhe
+49(0)721 6105 1315
linda.schindler@eifer.org