## Slide 1: EGU 7.5.2020 Case Pyhäsalmi underground mine
Rauno Heikkilä, University of Oulu, structures and Construction Technology

## Slide 2: MEASUREMENT EQUIPMENT USED
GeoSLAM Horizon
Leica Pegasus Backpack
Z+F Imager 5016

## Slide 3: MEASUREMENT METHODS AND DEVICES
Geoslam Horizon
  hanheld laser scanners (mobile)
  SLAM positioning
  reference points, georeferencing method
Leica Pegasus Backpack
  backbag scanner (mobile)
  positioning GNSS, inertia ja SLAM-tekniikka
  georeferencing GNSS or using reference points
Z+F Imager 5006
  terrestrial scanner (static surveying)
  positioning GNSS, inertia, adjustment of point clouds, total station
  georeferencing GNSS or using reference points

## Slide 4: MEASUREMENT OBJECT
Tunnel site, lenght 200 m
Tunnel profile width 5-9.4 m

## Slide 5: Measurement time and accuracy of positioning
Geoslam Horizon 25 min 5-50 cm/5-10 cm
Leica Pegasus Backpag 25 min 5-10 cm / 2-5 cm
Z+F Imager 5006 with total station 120 min 1 cm / < 1 cm
Z+F Imager 5006 with point cloud registration 120 min 1 cm / < 1 cm

## Slide 8: Triangulated surface