## Slide 1: The importance of an accurate estimation of the radiation balance and interception loss for the evaluation of evapotranspiration
Jitka Kofroňová, Václav Šípek, Miroslav Tesař
EGU, 2020
kofronova@ih.cas.cz

## Slide 2: Introduction
EVAPOTRANSPIRATION
= evaporation + transpiration
component of water balance
> 60% of precipitation is evaporated
potential (PET) X actual (AET)
it´s difficult to estimate PET + the accuracy is often questioned
many influencing factors: solar radiation, air temperature, wind speed, air humidity, vegetation, …
INTERCEPTION = capturing water on vegetation
  I = precipitation measured on the open area minus precipitation measured in the forest
currently: rarely measured or measured data rarely used
RESEARCH GAP
Hydrological modeling – both processes often included as simplified component
 such as coefficients, percent, equation, etc. (e.g. model SWAT – interception of the Norway spruce constantly 2,5 mm)
 influences the prediction of rate of other water balance components

## Slide 3: METHODOLOGY: Radiation + PET
FAO56 (Allen et al., 1998)
FAO24 (Doorenbos and Pruitt, 1977)
a1= 0,34 b1= 1,35 a2= -0,14 b2= 0,35
a1= 0,34 b1= 0,1
a2= -0,044 b2= 0,9
sensitivity analysis; statistics: RMSE, BIAS
PET
Penman-Monteith (1965)
+ tested other methods
Raditation
coefficients based on specific conditions  should be calibrated according to local conditions

## Slide 4: STUDY SITE
Experimentální povodí Liz (49°04´N, 13°41´E)
  monitoring since 1975
  longterm averages: 6,66°C, 851 mm
  radiation measured since 2009
  examined period: 2010-17
Daily and mean seasonal trend of radiation balance and its components – shortwave (SW) and longwave (LW radiation
Monthly and annual trends in air temperature, precipitation and PET

## Slide 5: RESULTS: Radiation
FAO56
RMSE: >1,4 MJ.m-2.day-1
 0,8-1 MJ.m-2.day-1
BIAS: 1-1,5 MJ.m-2.day-1
 +/-0,5 MJ.m-2.day-1
FAO24
RMSE: 1-1,5 MJ.m-2.day-1
 minimal changes
BIAS: +/-0,5 MJ.m-2.day-1
 both decrease and increase
Average daily deviation of modeled Rnl values against measured values (before and after calibration)

## Slide 6: RESULTS: PET
Different results shown also other methods for estimation of PET (PT - Pristley and Taylor, 1972, KP - Kimberley-Penman, 1982; TO - Thom and Oliver, 1977)
Without calibration: 40-80 mm difference in PET caused by FAO56 X only ~20 mm difference caused by FAO24
After calibration: FAO56 significantly improved in almost all examined years; FAO24 more accurate without calibration

## Slide 7: INTERCEPTION (I) - Methodology
  measurements: 1 raingauge in the open area, 5 raingauges randomly distributed in the forest
  5 commonly used approaches to evaluate I while using hydrological models: recalculation (model A)
    coefficient 2,2 mm (B)
    percent: I = 25% (C)
    percent: I = 35% (D)
    „linear reservoir“ with volume of 2,2 mm (E)
    „linear reservoir“ with volume of 3,3 mm (F)
  following simulations model HBV (Bergström, 1976)
   How will the different amount of interception affect other component of water balance, especially surface runoff (Q), soil moisture content (SMC) and groundwater height (GWHT)?

## Slide 8: INTERCEPTION (I) RESULTS
  all models underestimated the rate of interception except model A
  different interception sigificantly affected groundwater height (GWHT)
Runoff (Q), soil moisture content (SMC) and groundwater height (GWHT) trends under different interception amounts during growing season of 2018

## Slide 9: DISCUSSION
In this study:
  overestimation of the FAO56 method in our conditions, resulting in overestimation of PET
    the need of coefficient calibration  FAO56 significantly improved
  in general, FAO24 barely used
  the rate of different interception amounts influences the components of hydrological balance
GENERALLY:
  the problem of accuracy: the more input parameters (calculated, not measured) the greater probability of inducing a systematic error in estimation
    radiation one of the most important factors (the main source of the energy) its component – longwave radiation – is rarely measured  Does it lead to systematic error in calculating of PET?
  hydrological models – commonly used with simplified input parameters

## Slide 10: Summary and conclusions
evapotranspiration one of the most important components of water cycle: difficult to measure  modeled  many approaches originated
longwave radiation rarely measured  also modeled
  2 main approaches: FAO56 & FAO24
  include several coefficients derived on specific conditions  the necessity of coefficient calibration for local conditions
errors in resulting PET decreased to max 20 mm/season after calibration
FAO56
– widely used
– the need of calibration
– after calibration: better corresponding with measured values
FAO24
– rarely used
 missing data of daylight hours
– more accurate before calibration
interception – often neglected but included as parameter in hydrological models
  it has significant influence on other components of water balance
  the best result was achieved by taking off of interception capacity

## Slide 11: Thanks for reading!