## Slide 1: A case study of 5th generation district heating and cooling based on foundation pile heat exchangers (Vejle, Denmark)
Søren Erbs Poulsen, Maria Alberdi-Pagola, Karl Woldum Tordrup, Davide Cerra, Theis Raaschou Andersen
VIA University College, Horsens
Vejle Fjernvarme
Abstract: EGU2020-4626

## Slide 2
“Design and performance of energy pile foundations”, industrial Ph.D. project, 340,000 euro
IDEA
BASIC RESEARCH
CONCEPTUALIZATION
APPLIED RESEARCH
SMALL PROTOTYPE
LARGE PROTOTYPE
SYSTEM PROTOTYPE
DEMO SYSTEM
FIRST DEMO
FULLY COMMERCIAL
“Sustainable, building-integrated heating and cooling supply for future resilient cities”, EUDP, 400,000 euro
2015
2016
2017
2018
2019
2020
2021
2022
2023
Energy piles for 5th generation district
heating and cooling (5GDHC)
2024
VIA R&D Buildings, Energy, Water & Climate
https://www.ucviden.dk/portal/da/publications/bygningsintegreret-varme-og-koeleforsyning-til-fremtidens-resiliente-byer(a182ae4e-f4cb-4a57-a7eb-d4923e75176f).html
Abstract
EGU2020-4626

## Slide 3: Case study area: Rosborg Ø
a) | b)
Ny Rosborg: Future residential area to be developed
Rosborg Ø
Building footprint
16,950 m2
Energy piles for 5GDHC
Abstract
EGU2020-4626

## Slide 4: Geothermal screening for 5GDHC
Boreholes and geophysical surveys
Geological model
Soil thermal properties
Thermogeological model
Dimensioning of 5GDHC
Abstract
EGU2020-4626

## Slide 5: 5GDHC modular temperature model
Darcy-Weisbach pipe flow model:
;
Pipe heat transport model:
Soil: Pipe fluid:
;
Energy pile heat transport model:
Surface temperature effects:
Topology
Mathematical model
Abstract
EGU2020-4626

## Slide 6: Building energy demand
Geotechnical limit
5GDHC fluid temperatures
Supportable liveable area 65,000 m2
3 floors
Office buildings
Residential buildings
Supportable liveable area 75,000 m2
4 floors
Abstract
EGU2020-4626

## Slide 7: Business case
Business case | Case 1: Office buildings | Case 2: Residential buildings
Energy piles cost per year | € 35,321.00 | € 99,638.76
District heating cost per year | € 232,360.96 | € 341,705.00
Savings from energy piles per year | € 197,039.96 | € 242,066.24
Total capital costs energy piles* | € 2,950,742.60 | € 3,057,727.40
Total capital costs district heating* | € 2,209,261.60 | € 1,535,601.60
Payback period | 3.76 years | 6.29 years
Abstract
EGU2020-4626
Traditional district heating and air conditioning serve as reference when calculating the payback period