## Slide 1: Reducing uncertainty in emission estimates using perturbed emissions ensembles and novel observations: A focus on Beijing
Le Yuan1, David Carruthers2, Christina Hood2, Roderic L. Jones1, Olalekan A.M. Popoola1, Jenny Stocker2, Alexander T. Archibald1,3
1Department of Chemistry, University of Cambridge, UK
2Cambridge Environmental Research Consultants, Cambridge, UK
3National Centre for Atmospheric Science, UK
04/05/2020
ly299@cam.ac.uk

## Slide 2
Background
Why are there uncertainties in emissions inventories?
  Inherent uncertainties, e.g. input data, spatial proxies
  Uncertainties in emission trends, particularly in regions undergoing rapid changes
Why is reducing such uncertainties important?
  Uncertainties in emissions → uncertainties in air quality simulations → uncertainties in health/policy impact assessments
ly299@cam.ac.uk

## Slide 3
What is a perturbed emissions ensemble (PEE)?
Parameter | Initial PEE |  | Optimised PEE | 
 | Min. | Max. | Min. | Max.
Industry sector ground level CO emissions* | 0.3 | 1.8 | 0.1 | 1.8
Industry sector elevated CO emissions* | 0.3 | 1.4 | 0.1 | 1.4
Power sector CO emissions* | 0.2 | 1.5 | NA | NA
Power sector CO emissions below 150 m* | NA | NA | 0.1 | 1.8
Power sector CO emissions upper 150 m* | NA | NA | 0.1 | 1.8
Residential sector CO emissions* | 0.3 | 1.5 | 0.1 | 1.5
Transport sector CO emissions* | 0.4 | 2 | 0.1 | 1.5
Industry sector, ground level NOX emissions* | 0.4 | 1.6 | 0.05 | 1.6
Industry sector, elevated NOX emissions* | 0.4 | 1.4 | 0.05 | 1.4
Power sector NOX emissions* | 0.2 | 1.4 | NA | NA
Power sector NOX emissions below 150 m* | NA | NA | 0.05 | 1.6
Power sector NOX emissions upper 150 m* | NA | NA | 0.05 | 1.6
Residential sector NOX emissions* | 0.4 | 1.5 | 0.05 | 1.5
Transport sector NOX emissions* | 0.4 | 2 | 0.05 | 1.5
Transport sector night-time NOX emissions✦ | 0.1 | 0.5 | 0.1 | 0.3
Transport sector night-time NOX emissions✦ | 0.1 | 0.4 | 0.1 | 0.3
Determine emission parameters and their uncertainty ranges (via expert elicitation)
ly299@cam.ac.uk
*Defined relative to the base emissions
✦Defined as fraction of the daily total

## Slide 4
What is a perturbed emissions ensemble (PEE)?
Determine emission parameters and their uncertainty ranges (via expert elicitation)
Sample the parameter space (e.g. using maximin Latin hypercube design)
ly299@cam.ac.uk

## Slide 5
What is a perturbed emissions ensemble (PEE)?
Determine emission parameters and their uncertainty ranges (via expert elicitation)
Sample the parameter space (e.g. using maximin Latin hypercube design)
Input the perturbed emissions inventories to an air quality model
ly299@cam.ac.uk
Base emissions

## Slide 6
How can a PEE be used to constrain emissions uncertainties?
ly299@cam.ac.uk

## Slide 7
How can a PEE be used to constrain emissions uncertainties?
ly299@cam.ac.uk
variance
bias2
Min. achievable
MSE
Use the median mean square error (MSE) of a PEE member to represent its average performance across the model domain
MSEs of the top performing PEE members dominated by min. achievable MSE, related to the observed variance

## Slide 8
How can a PEE be used to constrain emissions uncertainties?
Smaller parameter ranges determined by the top performing PEE members
Not all parameters can be constrained
ly299@cam.ac.uk

## Slide 9
Next steps
Evaluate PEE performance by season and site type – different results?
Make use of other observations: vertical and ground based low-cost sensor measurements
ly299@cam.ac.uk