## Slide 1
Demand-side Management of Peak Water Demands using Advanced Metering Infrastructure and Persuasive Games
Jorge E. Pesantez
Emily Zechman Berglund, Ph.D.
Monday May 4th, 2020

## Slide 2
Urban water demands typically show a peak in the morning and evening
The water demand curve should be flattened:
When peak consumption coincides with high energy tariffs, water treatment and distribution pose an economic burden to a utility.
In a constrained water system, demand-side management can play an important role to avoid shortages.
AMI provides tools for shifting the system peak demand to alleviate peak demands.

## Slide 3
Demand-side management
Demand-side management (DSM) strategies can effectively modify consumption patterns.
DSM is widely applied in the energy sector.
DSM can be applied to shift peak consumption in water systems, but this has not been fully explored in research or practice.

## Slide 4
How can we promote consumer participation in DSM?
Diurnal water demand
AM
PM
NOON
$
$$$
$$
$$$
$
$
Dynamic Pricing
Smart meter data allows the implementation of dynamic pricing.
Serious Game
Online games to promote water conservation
Gamification
Leaderboard: customers earn points and improves their virtual ranking
Adapted from the SmartH2O project

## Slide 5
Gamification is enabled by feedback from smart meters
Drinking Water Pipes
High water use
Conservation suggestions
Hourly demands reported at smart meters
Encourage demand shifting of certain end-uses
System-level peak consumption identified by the utility
High water use
Conservation suggestions
High water use
Conservation suggestions
OD-Gamification:
Peer to peer communication about conservation

## Slide 6
Gamification in WDS
The Leaderboard works as follows:
Users receive instructions from the utility about shifting certain uses.
Users compete against each other within a neighborhood.
Each user can see his ranking on the leaderboard.
Leaderboard game
Adapted from the SmartH2O project

## Slide 7: Agent-based Modeling
ABM is applied to simulate the interaction between water utility and users, and between users to shift the system’s daily peak demand.
  Complexity: agents interact in multiple ways and follow local rules
  Emergence: behavior emerges when agents interact
  Adaptive: capacity of the system to adjust or to respond to consequences

## Slide 8
New information changes opinions, which changes behaviors
Do I change my showering time tomorrow?
What did I do yesterday?
Sources of information
Social media
Neighbors: word of mouth
Global broadcast
User opinion and actions change over time
Leaderboard

## Slide 9
Opinion Dynamics
The opinion of a person is affected by different sources of information.
The opinion changes over time.
An opinion leads to a decision.
If the opinion is greater than resistance, the decision is to shift water demand, otherwise, the decision is not to shift.

## Slide 10
Objectives
To simulate a demand-side management by the application of Opinion Dynamics (OD) and Gamification concepts through an agent-based model.
To develop an agent-based model to simulate a demand shifting program
To implement an OD model and a Gamification approach

## Slide 11
The opinion of an agent (household) is a function of the information obtained from global broadcast (Utility), social media, and neighbors.
*
*Adopted from Du, E., Cai, X., Sun, Z., & Minsker, B. (2017). Exploring the role of social media and individual behaviors in flood evacuation processes: An agent‐based modeling approach. Water Resources Research, 53(11), 9164-9180.
Where:
: opinion of agent j at time step t, continuous variable: O ϵ [0,1]
, , : learning rate and weighting parameters
: information obtained from global broadcast (=, where ϵ {0, 1})
: information obtained from social media
: information obtained from neighbor’s actions and communication
Opinion Dynamics Model

## Slide 12
: information obtained from social media:
: 0 or 1 within a social network of n agents.
: information obtained from neighbor’s actions:
: 0 or 1 within a neighborhood of nn neighbors.
at each time step, the agent will make a binary decision (X, X ϵ {0,1}) to shift the end-use () or not ().
OD: Modeling the information sources

## Slide 13
At any time step t, an agent j, will choose to shift his consumption if his opinion about shortage risk exceeds a risk-tolerance threshold :
Where is considered the highest value from the next table:
OD: Modeling information
Notes: At this point agent j has an opinion about shifting his water demand from the system’s peak hour to one of the options proposed by the utility. The options include different times of the day for different end-uses. The end-uses are showering, laundry, dishwasher, and outdoor watering.
This study considers different resistance values from the user to shift certain end-use represented by thresholds (T, T ϵ [0, 1]) (Beal et al 2016). Therefore, to proceed with a shift of any end-use: 𝑂_(𝑗,𝑡) > T. Table 1 shows the threshold values for each end-use and the time of use recommended by the utility.

## Slide 14
A combination of points and a leaderboard.
Depending on the shifted end-use, the user receives points using the rule:
Gamification: Leaderboard
is updated as follows:
if agent is Optimistic, = random (
if the agent is Conflicted, = random (
if the agent is Disengaged, =

## Slide 15
Number of customer agents: 30
Duration (days): 1000
Global broadcast from the utility (
Initial Opinion:
Model settings

## Slide 16
Preliminary Results
Opinion of a randomly selected agent
Without a leaderboard
,
,
With a leaderboard
,
,
Notes: At this point agent j has an opinion about shifting his water demand from the system’s peak hour to one of the options proposed by the utility. The options include different times of the day for different end-uses. The end-uses are showering, laundry, dishwasher, and outdoor watering.
This study considers different resistance values from the user to shift certain end-use represented by thresholds (T, T ϵ [0, 1]) (Beal et al 2016). Therefore, to proceed with a shift of any end-use: 𝑂_(𝑗,𝑡) > T. Table 1 shows the threshold values for each end-use and the time of use recommended by the utility.

## Slide 17
Preliminary Results
Opinion of a randomly selected agent
Without a leaderboard
With a leaderboard
Demand shifted of the agent
,
,
Notes: At this point agent j has an opinion about shifting his water demand from the system’s peak hour to one of the options proposed by the utility. The options include different times of the day for different end-uses. The end-uses are showering, laundry, dishwasher, and outdoor watering.
This study considers different resistance values from the user to shift certain end-use represented by thresholds (T, T ϵ [0, 1]) (Beal et al 2016). Therefore, to proceed with a shift of any end-use: 𝑂_(𝑗,𝑡) > T. Table 1 shows the threshold values for each end-use and the time of use recommended by the utility.

## Slide 18: Conclusions
Smart metered data were used to model a demand-side management (DSM) strategy to shift the system’s daily peak demand.
An agent-based modeling was built using the concepts from Opinion Dynamics and Gamification to implement the DSM strategy.
The effect of Gamification on the model adds variability to the agents’ opinion.
The new model that aims at flattening the diurnal demand curve to assist utilities in improving water distribution system operation.