## Slide 1
EGU2020 - Online, 4-8 May 2020
Understanding the importance of hydraulic head timeseries for calibrating a flow model:
Application to the real case of the Bacchiglione Basin (Veneto, Italy)
Mara Meggiorin1,2, Giulia Passadore1, Andrea Sottani2, Andrea Rinaldo1,3
1 Dipartimento di Ingegneria Civile, Edile e Ambientale, Università di Padova
2 Sinergeo Srl – Vicenza, Italy, info@sinergeo.it
3 Laboratory of Echohydrology (ECHO/IIE/ENAC), École Polytechnique Fédérale de Lausanne, Switzerland
EGU General Assembly 2020, Online
Sharing Geoscience Online, 4-8 May, 2020
!!! Session HS8.1.6 - Live chat on Monday, 04 May 2020, 08:30-10:15
Watch the video of the presentation HERE !!!

## Slide 2: Calibration for groundwater models
EGU2020 - Online, 4-8 May 2020
Groundwater moves through a heterogeneous subsoil
Detailed soil knowledge is impossible at large scales
Models need the optimization of hydrogeological properties
PEST calibrates property fields to reproduce observation data at best
By calibrating in transient conditions
It is possible to consider and fit different hydrological conditions
Intuitively,
more observations,
more the calibrated model will be reliable and preferable

## Slide 3: But…
EGU2020 - Online, 4-8 May 2020
Hydrogeological records often have missing values
Different choices on observation sampling time are possible:
By using daily data with missing values
By using monthly data that fastens also the model
Possible alteration of calibration process and parameters estimation
How and does it make a difference ??

## Slide 4: Analysis steps
EGU2020 - Online, 4-8 May 2020
Implement a flow model for a real case
Calibrate the model with different observation timeseries:
Results comparison:
Difficulties on visually inspecting 24 heterogeneous fields, therefore, calibrated hydrogeological properties are collated by:
  statistical distributions,
  simulated timeseries in two points within the observation area,
  sensitive analysis by estimating variation coefficients in pilot points.
Common settings for all scenarios:
model conceptualization
daily boundary conditions
Base model
(DD)
Missing data scenarios
(MDSc)
models simulating 20%, 40%, 60%, 80% and 100% missing data for each observation location
Sampling time scenarios
(STSs)
weekly data WD
monthly data MD
steady state SS
incomplete daily data
complete data
complete daily data - DD
considered the best achievable optimized model by using all available information
Calibrated properties:
Hydraulic conductivity / permeability (K)
Specific storage (S)

## Slide 5: Case study – subdomain of the Bacchiglione Basin
EGU2020 - Online, 4-8 May 2020
4 sensors continuously measuring the groundwater level
Unconfined groundwater system
Boundary conditions (BCs): northern and southern boundaries
    Dirichlet's conditions
  eastern and western boundaries
    no-flow boundaries
Records overlap for 783 days without missing data

## Slide 6: Case study – Water balance
EGU2020 - Online, 4-8 May 2020
Transient inflows:
Effective precipitation
defined thanks to a local weather station
River seepage
Timonchio river crosses the domain
the flow recharging the aquifer is estimated
by empirical formulas basing on the fluvial water level
Constant in and outflows:
Irrigation
channels of the irrigation public authority
do not vary between irrigation and not irrigation periods
4 public wells
constant flow rate
Private wells
their exploitations are estimated for each municipality

## Slide 7: Model implementation and calibration settings
EGU2020 - Online, 4-8 May 2020
FEFLOW
Mesh: small elements close to observation points, with sides of roughly 60m, enlarging up to sides of about 600m far away
3 model layers
Daily transient BCs
FEPEST
Transient calibration : 1 year
Pilot point estimation method
  pp denser close to observation points
  Kriging interpolation
Thikhonov regularization
SVD-Assist is applied as a fastening tool

## Slide 8: Results: Statistical descriptors – Hydraulic conductivity
EGU2020 - Online, 4-8 May 2020
Cumulative distribution functions

## Slide 9: Results: Statistical descriptors – Hydraulic conductivity
EGU2020 - Online, 4-8 May 2020
Main Observations:
STSs:
  Wide cumulative distribution functions (cdfs)
  DD has generally highest permeability values
  increasing the sampling time, cdfs move towards lower values with minimum values for the SS
  However, they all show similar curve shapes
MDSs:
  Their cumulative distribution functions are much more bunched up
  the complete absence of one observation timeseries leads to further curves, specially one of timeseries 4
  generally, there are small median discrepancies
  increasing the percentage of lacking data, all sensors lower the medians

## Slide 10: Results: Statistical descriptors – Specific storage
EGU2020 - Online, 4-8 May 2020
Cumulative distribution functions

## Slide 11: Results: Statistical descriptors – Specific storage
EGU2020 - Online, 4-8 May 2020
Main Observations:
STSs:
  Cumulative distribution functions move to higher values (for WD and MD)
  WD has a thinner range but higher median
  The optimization in steady state does not calibrate the property of specific storage, therefore SS model keeps the original homogeneous field
MDSs:
  Cumulative distribution functions have all similar shapes
  but they are moved in the x-axis (property values)
  increasing the missing data percentage, there is not an evident movement toward higher or lower values

## Slide 12: Results: Simulated hydraulic heads – point 1
EGU2020 - Online, 4-8 May 2020

## Slide 13: Results: Simulated hydraulic heads – point 2
EGU2020 - Online, 4-8 May 2020

## Slide 14: Results: Simulated hydraulic heads
EGU2020 - Online, 4-8 May 2020
Main Observations:
STSs:
  Trends of simulated heads are kept
  but heads are lower for MD and SS
    difference of almost 1m for SS
  WD simulates very similar hydraulic heads to ones of the base model DD
    an average difference of 1 cm
MDSs:
  Heads in both points are not affected by lacking data in sensors 2 and 3
    they can probably substitute each other
  But they are much more sensitive to sensors 1 and 4
    increasing the percentage of missing values, simulated hydraulic heads increase
    maximum discrepancy with DD for point 2 when there are not observations in sensor 4:
      heads difference of almost 2m

## Slide 15: Results: Properties heterogeneity within the observation area Sampling time scenarios
EGU2020 - Online, 4-8 May 2020

## Slide 16: Results: Properties heterogeneity within the observation area Missing data scenarios – sensor 4
EGU2020 - Online, 4-8 May 2020

## Slide 17: Results: Properties heterogeneity within the observation area
EGU2020 - Online, 4-8 May 2020
Main Observations:
STSs:
  permeability fields show differences on estimated values between DD and higher sampling intervals, but the heterogeneity structure is the same
    higher values are estimated by the base model
    the WD property values are very close
    MD and SS have the same heterogeneity but flattened
  specific storage estimated fields, instead, do not even show a similar structure
MDSs:
  permeability fields show similar heterogeneity structure and values
    K heterogeneity slightly flattens increasing the missing data percentage
    biggest difference when there is not observation in location 4
      there is no information for the northern sector
      the calibration process estimates a very low conductivity area
  also the estimated S fields show a similar structure

## Slide 18: Results: Uncertainty analysis
EGU2020 - Online, 4-8 May 2020
Goal:
understand the model uncertainty variability with different observations (optimization target)
  Therefore, the focus is on the difference between estimated fields of hydrogeological properties, mainly their assigned values to pilot points
  posterior Monte Carlo (pMC) analysis: calibration of 20 models starting from an almost calibrated condition
    the worst two optimized models of the pMC analysis are discarded
    CV evaluation: ratio between standard deviation and mean of 18 optimized values in each pilot point
For each pilot point
Lower the CV
Lower the parameter variability between calibrated models
Lower the local parameter uncertainty

## Slide 19: Results: Uncertainty analysis
EGU2020 - Online, 4-8 May 2020
K
S

## Slide 20: Results: Uncertainty analysis
EGU2020 - Online, 4-8 May 2020
K
S

## Slide 21: Results: Uncertainty analysis
EGU2020 - Online, 4-8 May 2020
Main Observations:
different uncertainty between the two hydrogeological parameters:
  all models show lower CVs for the hydraulic conductivity parameter
STSs show an increasing uncertainty for larger time intervals
MDSs instead do not see any uncertainty variation,
  each pilot point has different CVs for each scenario
  but there is not a recognizable general uncertainty trend by increasing the missing data percentage

## Slide 22: Conclusions - Varying the timeseries sampling interval
EGU2020 - Online, 4-8 May 2020
Increasing the sampling time, there is a progressive distancing from the base model with complete daily data
Permeability cdfs move towards lower values with minimum values for the SS
Specific storage cdfs move to higher values (for WD and MD)
Trends of simulated heads are kept but heads lower for MD and SS
Permeability fields show:
Same heterogeneity structure
WD property values are very close
MD and SS have flattened values
Specific storage estimated fields, instead, do not even show a similar structure
Increasing uncertainty for larger time intervals
STSs

## Slide 23: Conclusions - Missing values in one observation timeseries
EGU2020 - Online, 4-8 May 2020
Generally, smaller variations than sampling time scenarios
Permeability cdf are much more bunched up: the complete absence of one timeseries leads to further curves
Specific storage cdfs move in the x-axis (property values) without an evident trend
Simulated heads are more sensitive to sensor 1 and 4
higher heads increasing the percentage of missing values
K and S fields show similar heterogeneity structure and values
biggest difference when there is not observation in location 4 (no information for the northern sector)
There is not any uncertainty trend by increasing the missing data percentage
The model is more sensitive to timeseries in sensor 4 than others
All estimated fields with partial daily timeseries in sensor 4 are very similar both in terms of:
statistical descriptors
heterogeneity aspects on map
Seems like most important information tracked from this sensor is its mean level:
more than its trend
only the complete absence of information on that location makes a large difference
MDSs

## Slide 24: Groundwater modeling choices for observations in transient calibration
EGU2020 - Online, 4-8 May 2020
If daily timeseries are available,
it is preferable to use them even with missing data
Larger sampling times
slightly diminish the computational effort (BCs are still daily data)
But lead to loss of information and different estimated fields
the discrepancy can be acceptable or not depending on the model goal and scale
In this analysis, using weekly timeseries seems to be a good compromise,
most of results are comparable to ones of the base model
More studies are needed to confirm this

## Slide 25
FOR FURTHER
QUESTIONS
mara.meggiorin@dicea.unipd.it
mmeggiorin@sinergeo.it
EGU2020 - Online, 4-8 May 2020
EGU General Assembly 2020, Online
Sharing Geoscience Online, 4-8 May, 2020