## Slide 1
A multi-tiered methane analytic framework for constraining budgets, point source attribution, and anomalous event detection
Daniel Cusworth1, Riley M. Duren2,1, Vineet Yadav1, Andrew K. Thorpe1, Natasha Stavros1, and Charles E. Miller1
© 2020. All rights reserved
1Jet Propulsion Laboratory, California Institute of Technology, 2University of Arizona

## Slide 2
To get a clear picture of methane emissions, we need measurement and analytics strategies at all measurement scales.
Satellites:
- Regional scale
- Targeted point source
Tall tower networks
Airborne surveys
- e.g., AVIRIS-NG
On-road surveys
On-site surveys

## Slide 3
Satellite monitoring and data assimilation with the TROPOMI satellite instrument allows for sub-basin scale quantification of methane emissions.
TROPOMI XCH4 over TX, NM, OK
Delaware Permian Basin
XCH4 (ppb)
10
7.5
5.0
2.5
0
Emission Flux rate (t/h)
Flux inversion
Duren, Cusworth, Thorpe, et al. in prep

## Slide 4
A well-spaced system of tower sites also allows for basin-scale emissions monitoring.
Los Angeles Megacities Carbon Network
Yadav et al., JGR, 2019
Results of flux inversion
Inverse results sensitive to two major events:
(1) Aliso Canyon blowout (2) Closing of Puente Hills Landfill
Notes: Example of methane flux inversion (emission map) from persistent regional monitoring from the LA Megacities surface network. In this case, this is a WRF-STIL inversion for 2015 and 2016 at 3km resolution, 4 day time step (interpolated here). The redder contours show higher emitting areas with some notes about major infrastructure. The scale on this plot is the entire LA basin – about 100km x 100km. While uncertainties are large in single grid cell emission estimates we can split the basin in 5 zones/bins and compare the inversion posterior results with prior emission inventories.

## Slide 5
Anomalous super-emitters at <0.2% of infrastructure are responsible for 35-43% of California CH4 inventory (0.541-0.674 TgCH4 y-1, 95% CI)
Airborne surveys capture a key ingredient missing from regional flux inversions – direct attribution of point source emissions.
California Methane Survey
AVIRIS-NG imaging spectrometer:
- Detection of point sources 5-10 kg h-1
- Gives 3 m spatial maps of plumes
Duren et al., Nature, 2019
Notes: 5 months of flights 2016-2018; repeat overflights of >272,000 facilities and components; 562 sources

## Slide 6
Moving from disparate single-tiered systems to a multi-tiered system:
How do we leverage all this information into one data system?
Cusworth et al., GRL, 2020

## Slide 7
How do we combine these data streams together?
Multi-tier data assimilation
Independent point source flux quantification
Towers
CLARS-FTS
TROPOMI
AVIRIS-NG
Flight planning
Validation

## Slide 8
Total basin sensitivity to emissions depends on type of instrument and spatial/temporal density
Footprints (∂F/ ∂x) simulated using HRRR-STILT tracer-transport model
Though TROPOMI is less sensitive to surface emissions, it has greater spatial coverage throughout the basin.

## Slide 9
All observations and footprints can be brought together in an inverse modeling framework to optimize gridded flux emissions:
Sunshine Canyon Landfill, Aliso Canyon oil/gas
Sunset/Hunington beach oil/gas fields
San Gabriel Mountains

## Slide 10
We can use the inverse result to target specific areas. Case study: Sunshine Canyon Landfill
Emissions around Sunshine Canyon higher than EPA prior early in study period
This tells us where to go fly AVIRIS-NG
AVIRIS-NG Sunshine Canyon Landfill
March-April 2017
Massive methane plumes emanating from intermediate slopes.

## Slide 11
Sunshine Canyon then underwent expensive infrastructure investments to reduce these emissions.
Solution: Apply ClosureTurf (e.g., artificial grass), PosiShell (cement, bentonite, fiber spray mix), or compacted vegetative cover to problematic slopes.
ClosureTurf
PosiShell
Compacted cover
Feb 2017
June 2017
Feb 2019

## Slide 12
Improvements were validated by AVIRIS-NG. Odor complaints were reduced as well!
Methane plumes after infrastructure improvements
Trend in intermediate slope IME and odor complaints
IME: Measure of excess methane plume mass retrieved by AVIRIS-NG
Cusworth et al., ERL, 2020

## Slide 13
This reduction in emissions was also observed from the multi-tiered inversion.
AVIRIS-NG derived emission rate
Trend in Sunshine Canyon methane emission rate
in 3 km grid containing Sunshine Canyon
March-April 2017
March-April 2018

## Slide 14
This type of system can be readily expanded to cover CO2 sources. AVIRIS-NG CO2 retrievals shows close correspondence with bottom-up reporting.
Cusworth et al., in prep
Extensible to countries where little bottom-up reporting exists.
Udupi Power, India

## Slide 15
Conclusions
Multiple independent methane observations can be synthesized on a regional scale via a data assimilation / lagrangian transport model system.
Independent AVIRIS-NG flights at Sunshine Canyon Landfill corroborated inverse fluxes from the multi-tiered inverse system.
Future spaceborne imaging spectrometers will be able to detect very large methane sources.
This approach is readily extensible to CO2 monitoring