## Slide 1
Escape, Plasma and Acceleration Dynamics Explorers
ESCAPADE
Rob Lillis, Shannon Curry, Janet Luhmann, Aroh Barjatya, Davin Larson, Christopher Russell, Roberto Livi, Phyllis Whittlesey, Yingjuan Ma, Ronan Modolo, Yuki Harada, David Brain, Paul Withers, Christopher Fowler, Shaosui Xu, and Ed Thiemann
1
EGU Virtual meeting, May 5, 2020
* I won’t be awake for the chat so please email me with any questions: rlillis@berkeley.edu
Notes: The last several talks showcased the rich array of plasma processes occurring in the Mars magnetosphere, and form a great motivation for my talk. I’ll talk about the science case for ESCAPADE, as well as our mission for the mission including instruments, spacecraft, and mission design

## Slide 2: ESCAPADE 30-second summary
What is it? Two identical smallsats, measuring plasma conditions from coordinated elliptical Mars orbits.
Why? Understand how solar wind energy and momentum are transferred through the Martian magnetosphere, and the consequences for plasma-related atmospheric escape.
How? Selected as part of the SIMPLEX-II program. Ride-share with the Psyche mission. Electric propulsion + aerobraking.
When? Launch 08/22, Science 07/24-07/25.
How much? < $55 million

## Slide 3: The Martian plasma environment: why do we care?
Understand structure, composition, variability and dynamics of a unique hybrid magnetosphere.
Atmospheric Escape Processes: ion and sputtering escape are important the evolution of Mars’ climate.

## Slide 4: Q: Why ESCAPADE?
A: A single measurement platform leaves major questions unanswered
spatial and temporal plasma variations cannot be distinguished
responses of magnetosphere & escape to changing heliospheric conditions (~1 minute) can only be measured with a time-lag of an hour or (much) more
Multi-point in situ observations from coordinated orbits are required to untangle spatial from temporal variability and characterize real-time response to heliospheric drivers.
Notes: The figure on the bottom shows the evolving orbit of MAVEN in MSO coordinates, or with respect to the sun, showing the nominal location of the various plasma regions and boundaries. Black is the undisturbed solar wind, behind which is the bow shock and the magnetosheath region where the solar wind plasma slows down, heats up, becomes turbulent and diverts around the conducting obstacle of the ionosphere. The yellow region is where the interplanetary magnetic field piles up and drapes around the planet. The blue region is the wake where the double-lobed magnetotail trips behind the planet. This is a highly simplistic representation of a very complex picture that displays enormous variability as the properties of the solar wind change: density, velocity, IMF magnitude and IMF cone and clock angle.

## Slide 5: Spatial-Temporal Ambiguity
Boundary Processes:
  Snowplow Bulk Plasma Loss on the IMB [Halekas et al., 2015, 2016].
  Kelvin-Helmholtz Instabilities [Ruhunusiri et al., 2017]
  Bow shock motion.
3-D structures evolving in time:
  Flux Ropes [Hara et al] & plasmoids.
Field-aligned potentials:
  Double layers & Inverted-V signatures [Xu et al., 2019].
Ionospheric processes:
  Irregularities [e.g. Fowler et al., 2018] & ion heating
  Magnetic Cusp influences.
  Electron precipitation
Notes: The interaction of unmagnetized planetary heavy ions with magnetized sheath protons results in polarization electric fields at the edges of the unmagnetized bubble as ions try to freely propagate, and resulting shielding currents which pile up the magnetic field in a snowplow effect. The structure is likely dynamic in space and time , and ions are accelerated to different energies, resulting in energy dispersion.
All these features of the Mars-SW interaction are likely dynamic in space and time. Multi-point observations will untangle space & time and elucidate these processes.

## Slide 6: Response to solar wind conditions
Categorizing ion loss or precipitation by SW/IMF conditions relies on once-per-orbit proxies or assuming SW conditions are steady over 1-3 hours.
Bad assumption when pressures exceed 1-2 nPa.
Real-time response to impulsive events cannot be characterized.
Dubinin et al., 2017
Marquette et al., 2018

## Slide 7: ESCAPADE
ESCAPADE is a twin-spacecraft Class D mission dedicated to studying the transfer of solar wind energy and momentum through Mars’ unique hybrid magnetosphere and how it drives ion and sputtering escape.
Builds on MAVEN’s legacy for a fraction of the cost.
In June 2019, ESCAPADE was selected for Phase A&B funding as part of the NASA SIMPLEX program.

## Slide 8: ESCAPADE Goals & Objectives
Goal A. Understand the processes controlling the structure of Mars’ hybrid magnetosphere and how it guides ion flows. A1. Determine magnetic structure and plasma flows in Mars’ magnetotail and how they vary spatially, temporally, and with respect to solar wind conditions. A2. Determine structure in Mars’ ion escape plume and how it varies spatially, temporally and with respect to solar wind conditions. | Goal B. Understand how energy and momentum is transported from the solar wind through Mars’ magnetosphere. B1. Measure the flow of mass and energy from the solar wind across Mars’ bow shock to the magnetosheath. B2. Measure the flow of mass and energy within Mars’ magnetosheath and from it across the magnetic pileup boundary into the upper ionosphere. B3. Measure the flow of mass and energy between day and night in the upper ionosphere. B4. Measure the flow of mass and energy from Mars’ magnetosheath across the flanks into the magnetotail. | Goal C. Understand the processes controlling the flow of energy and matter into and out of the collisional atmosphere. C1. Measure plasma outflow and precipitation in Mars’ upper ionosphere, and how they vary spatially, temporally and with respect to solar wind conditions and crustal magnetic fields.

## Slide 9: Measurements & Instruments
Magnetic Fields (DC) | Suprathermal Ions | Suprathermal Electrons | Thermal Plasma Density | Solar EUV flux (55-130 nm)
Range: 0 - 103 nT Magnitude Accuracy: 0.5 nT Direction Accuracy: 20°, ¦B¦ > 1 nT Cadence < 1 s (< 1000 km) < 2 s (> 1000 km) | Energy: 2 eV - 20 keV (25% ΔE/E) Angles: 2.8p (30° x 30°) Mass: M ≤ 4, M ≥ 16 Eflux: 3x105-1010±30% Cadence: < 20 s (< 1000 km) < 40 s (> 1000 km) | Energy: 3 eV - 10 keV (25% ΔE/E) Pitch angle: 20 - 160°, 30° resolution Eflux:104-5x109 ±30% Cadence: < 20 s (< 1000 km) < 40 s (> 1000 km) | Range: 20-3x104 cm-3 Accuracy: 30% Cadence: < 20 s (< 1000 km) < 40 s (> 1000 km) | Flux: 0.005-0.02 W/m2 Relative accuracy: 10% Cadence: <1 hour
EMAG (UCLA) Lead: C. Russell | EESA-i (UCB-SSL) Lead: R. Livi | EESA-e (UCB-SSL) Lead: P. Whittlesey | ELP-mNLP (ERAU) Lead: A. Barjatya | ELP-PIP (ERAU) Lead: A. Barjatya
Threshold Mission
Notes: Instrument trades are underway already.

## Slide 10: Science Drives Spatial/Temporal separation
Bow Shock
Solar wind
Magnetosheath
Magnetic Pileup Boundary
Tail
Ionosphere
Day
Night

## Slide 11: Science Drives Spatial/Temporal separation
Bow Shock
Solar wind
Magnetosheath
Magnetic Pileup Boundary
Tail
Ionosphere
Day
Night

## Slide 12
Bow Shock
Solar wind
Magnetosheath
Magnetic Pileup Boundary
Tail
Ionosphere
Day
Night
Science Drives Spatial/Temporal separation

## Slide 13: Science Drives Spatial/Temporal separation
Bow Shock
Solar wind
Magnetosheath
Magnetic Pileup Boundary
Tail
Ionosphere
Day
Night

## Slide 14: ESCAPADE Science Phase
Science Campaign A
7/1/24 – 1/1/25
Periapse altitude: | 200 | km
Apoapse altitude: | 7000 | km
Inclination: | 60 | deg
Period: | 4.9 | hours
Periapse altitudes: | 200, | 200 | km
Apoapse altitudes: | 8600, | 5600 | km
Inclinations: | 60, | 60 | deg
Periods: | 4.24, | 5.85 | hrs
Science Campaign B
2/1/25 – 8/1/25

## Slide 15: Orbital Evolution

## Slide 16: Orbital Evolution

## Slide 17: ESCAPADE is Timely

## Slide 18: ESCAPADE Spacecraft (x2)
EESA-electrons
EESA-ions
EMAG
ELP

## Slide 19: ESCAPADE Mission Design
30
Modeled effective thrust (mN)
1st captured orbit
2nd orbit
3rd
4th
Sun
1. Launch:
Psyche launch
Date: 8/(6-26)/2022
C3: 14.53 km2/s2
RLA: 72.96 deg
DLA: 1.783 deg
2. Spacecraft Checkout
3. Initial Thrust
ESCAPADE thrust vectors
Psyche’s Mars Flyby: 5/2023
Psyche’s Trajectory (dashed)
5. Cruise
Active SEP
6. Mars Rendezvous
1/29/2024
9. Aerobraking Walk-In 4/1/2024
10. Science Orbit
7/1/2024
4. Coast
8. Active Orbit Reduction
Maximum available effective thrust
Modeled effective thrust: 85% duty cycle
Thrust arcs in red
7. Mars Arrival
8. Active Orbit Reduction
10. Aerobraking Main Phase
11. Aerobraking Exit
12. Spiral to Science
Extended mission

## Slide 20: ESCAPADE Team
PI: R. Lillis
DPI: J. Luhmann
PS: S. Curry
PM: D. Curtis
MSE: E. Taylor
ISE: S. Courtade
Lead: D. Larson
EESA-e: P. Whittlesey
EESA-i: R. Livi
Lead: C. Russell
Deputy: Y. Ma
Lead: M. Lewis
Nav: D. Cosgrove
Lead: J. Parker
Lead: A. Barjatya
Lead: B. Williams
Leadership/PM/SE
EESA
Ops
EMAG - UCLA
Mission Design – Advanced Space LLC
ELP – Embry Riddle
D. Brain (LASP)
Y. Harada (U. Kyoto)
R. Modolo (CNRS)
C. Fowler (UCB)
S. Xu (UCB)
Spacecraft – Tyvak LLC
Science Team
UCB Space Sciences Lab

## Slide 21: ESCAPADE Status/Timeline
Phase B underway. Funded by NASA Heliophysics Division. Not in competition.
Reviews completed:
  Requirements peer review.
  Mission Design peer review
  Instruments peer review
Reviews coming up
  Spacecraft peer-review May.
  Operations peer-review early June.
  Formal Planetary Design Review July 21-22nd.
  NASA Confirmation Review & KDP-C August 2020.
Launch mid-August 2022, rideshare with Psyche.

## Slide 22: Summary
ESCAPADE’s multi-point measurements are the only way to separate spatial and temporal variability & unravel cause-and-effect in Mars’ solar wind interaction and plasma-related escape.
ESCAPADE’s instrument suite and mission design enable this groundbreaking science.
The team is excited to move towards a detailed design and PDR in summer 2020 and prove that high-value science can be done for low/moderate cost.

## Slide 23: Backup slides

## Slide 24: SIMPLEX Programmatics
Three Selections from 12 Proposals.
All 3 managed by PMPO at MSFC.
Heliophysics Division (HPD) funding ESCAPADE Phase A/B. Prog. Sci. and Exec. From HPD.
Not a competition as of September 4.
  Funded by different divisions (HPD, PSD, LDEP)
  Evaluated Separately
Same SRB (mostly) will evaluate all three.

## Slide 25: Science Enhancement Options
Radio Occultation (P. Withers)
  Baseline is direct to Earth. Similar to MAVEN occurrence (x2).
  Examining SC to SC (looking unlikely due to radio hardware limitations)
Lower Altitude Periapsis:
  ~200 km periapsis (like MAVEN post-09/2020) is adequate to characterize ion flows in the magnetosphere.
  ~150 km periapsis requires more nav/ops support ($$).

## Slide 26: Response to solar wind conditions (1)
How does the system respond in real-time to disturbances like SIR/CIRs & heliospheric current sheet crossings?
Examples exist but they are fortuitous.
Harada et al., 2017

## Slide 27: ESCAPADE cooperation with MAVEN
Assuming MAVEN is healthy ~late 2022, ESCAPADE:
  Could tweak science orbits during cruise (power constraints notwithstanding) to maximize coordination.
  Could extend Science Campaign A (pair-of-pearls on string).
Science team is a) 100% MAVEN folks, b) very small (v. limited $$)
ESCAPADE won’t be able to afford analysis to make full use of data. Need to work across missions to develop tools for multi-point analysis.
If/when ESCAPADE confirmed, makes sense to invite others to science team meetings to develop multi-point data analysis techniques to prepare for data.

## Slide 28: Response to Solar Storms
Curry et al., 2019 (in review)
Notes: Somewhat related