## Slide 1: Lander Radioscience (LaRa) in ExoMars 2020 to obtain the rotation and orientation of Mars.
Véronique Dehant1, Rose-Marie Baland1, Sébastien Le Maistre1, Ozgur Karatekin1, Marie-Julie Péters1, Attilio Rivoldini1, Ertan Ümit1, Tim Van Hoolst1, Marie Yseboodt1, William M Folkner2 and Alexander Kosov3
(1) Royal Observatory of Belgium, Brussels, Belgium,
(2) Jet Propulsion Laboratory, United States,
(3) IKI Space Research Institute of the Russian Academy of Sciences, Moscow, Russia
EGU2020-6566
2022

## Slide 2
X-band radiolink
Uplink in [7.145,7.190] GHz
Downlink in [8.400,8.450] GHz
Coherent
transponder
maser
Objectives of LaRa:
Rotation and interior of Mars
and habitability
Past
Present?
Present? or future?
liquid core
EGU2020-6566

## Slide 3: 1. LaRa development status report
PDR 2017, CDR 2018
Compatibility tests at ESOC 2018:
Excellent ADEV performance!
Delivery 2019
EGU2020-6566
targeted value
obtained value
Notes: Perfo one order of mag

## Slide 4: 2. Ground stations
Baseline ground stations to close link with LaRa (5 Watt out) is NASA DSN – 70m antennas
Operational needs: twice a week for one hour
EGU2020-6566
Notes: Explain while we need all three.
Requirement docu to be sent to PRODEX

## Slide 5: 3. Mission geometry
Time (years)
SEP = Sun-Earth-Probe angle (elongation)
Pink boxes: Small Sun-Earth-Probe angle (= elongation), meaning a larger noise on the data
Grey boxes: Small Earth declination
EGU2020-6566
Notes: Define declination
The gray boxes for the Earth declination correspond to time intervals where the Earth declination is smaller than 10°, which means that the sensitivity to Mars spin axis motion in space is smaller at that time.
The InSight nominal mission lifetime is shown with the orange bar.
The black part of the curve being the points where the SEP angle < 15°, corresponding to data with a large noise due to the solar plasma. This corresponds to the interval July-October 2019.
Pink box = Doppler data noise increased near conjunction: here for SEP angle less than 15°

## Slide 6: 4. Expectations
LaRa is a Belgian instrument selected on the ExoMars surface platform of Roscosmos/ESA mission.
LaRa will provide information on interior of Mars, its evolution, as well as CO2 sublimation/ condensation process between the atmosphere and the ice caps.
synergies between InSight / RISE and LaRa are very valuable;
synergies with all atmospheric data are very valuable too.
EGU2020-6566

## Slide 7: 5. Expected results (1)
Mars Orientation Parameters (MOP) | Model | Max. MOP amplitude | Max. change in the lander position | Geophysical Properties
Nutation in obliquity () | Trigonometric series (annual, ½, 1/3, …) | 10 m | 10 m | Cf (Mars core moment of inertia) Core state, core size, core density
Nutation in longitude () | Trigonometric series (annual, ½, 1/3, …) | 30 m | 12 m | 
Liquid Core effect | Liquid core amplification in the nutations | 0.7 m on d, 0.4 m on d | 0.4 m | 
Precession Rate (uncertainty of 2 mas/y) | Rate | 0.8 m | 0.8 m | C (Mars moment of inertia)
Length-of-day (LOD) variations | Trigonometric series (annual, 1/2, 1/3, …) | 12 m | 12 m | Atmosphere and ice caps dynamics
Polar motion (PM) | Trigonometric series | 1.2 m | 1.2 m | 
EGU2020-6566
Notes: Since the Free-Core-Nutation (FCN) periods of the Mars models lie between the periods of the retrograde semi-annual and ter-annual rigid nutations (-343.5 days, -229 days), those nutations are the most affected by the liquid core.

## Slide 8: 5. Expected results (2): Nutation estimates
Estimated uncertainties on the amplitudes of the semi-annual prograde nutation and ter-annual retrograde nutation as a function of the mission duration.
The uncertainties are superimposed with the expected effect that a planet with a liquid core would have on those nutations (grey boxes).
These predicted uncertainties will be further reduced when combining LaRa’s data with InSight-RISE data.
EGU2020-6566

## Slide 9: 5. Expected results (3): Nutation estimates
Measurement of the nutation parameters (in particular the ter-annual retrograde amplitude) will allow us to constrain the size of the Martian core as well as its moment of inertia and flattening.
EGU2020-6566

## Slide 10: 6. Determination of the position of the lander
LaRa alone can be used to estimate the coordinates (including Z) of the ExoMars 2020 Surface Platform (SP) at the level of tens of meters after only two days of DTE Doppler tracking operations.
EGU2020-6566
Notes: An early estimate of the lander location will certainly improve the quality of the science analysis (for instance by making easier the recognition of the geological features seen on the lander's pictures) and allow high resolution cameras from spacecraft to correctly target
the lander.

## Slide 11: Thank you for your interest!!!! Acknowledgements
This work was financially supported by the Belgian PRODEX program managed by the European Space Agency in collaboration with the Belgian Federal Science Policy Office.
EGU2020-6566