## Slide 1
EGU2020 - Online, 4-8 May 2020
Comparison of two methods for optimizing existing groundwater monitoring networks:
Application to the real case of the Bacchiglione Basin (Veneto, Italy)
Andrea Sottani1, Mara Meggiorin1,2, Luís Ribeiro3, Andrea Rinaldo2,4
1 Sinergeo Srl – Vicenza, Italy, info@sinergeo.it
2 Dipartimento di Ingegneria Civile, Edile e Ambientale, Università di Padova
3 CERIS, Instituto Superior Técnico, Lisbon University, Av. Rovisco Pais, Lisboa Codex, Portugal
4 Laboratory of Echohydrology (ECHO/IIE/ENAC), École Polytechnique Fédérale de Lausanne, Switzerland
EGU General Assembly 2020, Online
Sharing Geoscience Online, 4-8 May, 2020
!!! Session HS8.2.9 - Live chat on Tuesday, 05 May 2020, 14:00-15:45
Watch the video of the presentation HERE !!!

## Slide 2
EGU2020 - Online, 4-8 May 2020
I’d like to thank Professor Luìs Ribeiro who unfortunately passed away on April 3rd, 2020
My professor and master thesis co-supervisor: he was a great teacher who made me discover, enjoy and get passionate in groundwater
I thank him for his help with this paper and guidance
on theoretical development, results comprehension and evaluation, particularly on the Hierarchical clustering method
Some of his major contributions to sciences are:
Evaluation of an intrinsic and a specific vulnerability assessment method in comparison with groundwater salinisation and nitrate contamination in two agricultural regions in the south of Portugal
Application of a groundwater quality index as an assessment and communication tool in agro-environmental policies–Two Portuguese case studies
Probably his major contribution remains his strong international commitment, particularly in Latin American countries, where he devoted himself to the social implications of water management

## Slide 3: Groundwater Level Monitoring Networks (GLMNs)
EGU2020 - Online, 4-8 May 2020
Collect crucial information
for evaluating groundwater sustainability,
for implementing an integrated water resources management
But
Monitoring is expensive
Economic considerations influence the number of monitoring wells
Designing a GLMN is a compromise between
prediction accuracy
cost minimization
To reduce costs:
Less sensors
Lower sampling frequency

## Slide 4: Optimization of Groundwater Level Monitoring Networks
EGU2020 - Online, 4-8 May 2020
The statistical analysis of recorded measurements from existing groundwater monitoring networks can:
Improve the knowledge of the groundwater system
Evaluate the existing network
Optimize and enhance its efficiency
Comparison of two statistical optimization methods:
Oscillations correlation method
Hierarchical clustering of
Average yearly hydrograph
Principal Components
Monthly trends

## Slide 5: Case study – Bacchiglione Basin
EGU2020 - Online, 4-8 May 2020
VICENZA
Asiago
Monti Lessini
Brenta
Remarkable water asset:
drinkable water to people in Vicenza and part of Padua
dense network of residential, industrial and agricultural areas
Important to preserve, protect and rationally use the groundwater resource
N
S
N
S
L. Altissimo, A. Dal Prà and G. Scaltriti, 1999 - Modified

## Slide 6: Sinergeo’s Groundwater Level Monitoring Network
EGU2020 - Online, 4-8 May 2020
VICENZA
THIENE
SCHIO
BASSANO DEL GRAPPA
102 sensors
(many with CPRS module)
Not homogeneous series:
Not uniformly distributed in space
Recording periods not simultaneous
    outliers removal
        hourly to daily data
        check of series length
        interpolation
        check of stationarity
        79 timeseries

## Slide 7: Oscillation correlation - Steps
EGU2020 - Online, 4-8 May 2020
Estimate detrended timeseries
Evaluate oscillations timeseries correlation two by two
Pearson correlation coefficient
Kolmogorov-Smirnov test for highly correlated series
Group intercorrelated couples
Produce a group map
1
2
3
4

## Slide 8: Oscillation correlation method
EGU2020 - Online, 4-8 May 2020
Estimate detrended timeseries
Evaluate oscillations timeseries correlation two by two
Pearson correlation coefficient
1
2
Easy to use but
poor statistic for variables not linearly correlated
If timeseries are correlated they seem to be linearly correlated
For linear correlation

## Slide 9: Oscillation correlation
EGU2020 - Online, 4-8 May 2020
Kolmogorov-Smirnov test
3
Pearson correlation coefficient
2
25 vs 40
Corr=0.694
25 vs 32 Corr=0.995
Example
For highly correlated timeseries
Their sample distribution functions are compared
No assumptions are made on variables or sampling error distributions

## Slide 10: Oscillation correlation
Group intercorrelated couples
4
EGU2020 - Online, 4-8 May 2020
Correlation map
All sensors inside an area have highly correlated hydraulic head timeseries
(c>0.95)
Similar hydrgeological behavior
9 clusters
42 not clustered sensors

## Slide 11: Hierarchical clustering - Steps
EGU2020 - Online, 4-8 May 2020
Define type of the input data For each sensor:
Yearly average hydrograph
Complete timeseries of 5 years only 60 sensors
Seasonal trends
Mann-Kendall test
Sen’s slope estimator
PCA
PCA
Hierarchical clustering
Seasonal trends
Yearly average hydrograph
PCA components
All previous variables
1
2
3
PCA – Principal Component Analysis

## Slide 12: Hierarchical clustering – Detailed Steps
3 PCA with different inputs data
2
EGU2020 - Online, 4-8 May 2020
Input data
Yearly hydrograph
Complete series
Seasonal trends
Mann-Kendall
Non-parametric test, statistically determines if a variable has increasing or decreasing values
Sen’s slope
Estimates the trend slope, robust against outliers
1
Hierarchical clustering groups data over a variety of scales by creating a cluster tree
it is an unsupervised technique with multiple choices
4 clustering with different input data
Yearly hydrograph
Seasonal trends
PCs
All together
no assumptions on data
reduces dataset dimensionality losing as less information as possible
is simply an orthogonal transformation of original variables into few linearly uncorrelated variables, principal components (PCs)
first PC accounts for most of the data variability and following PCs have the highest left variability
here selected first n PCs explaining more than 80%
remaining PCs contain much less information and may be considered as noise
useful for detecting patterns
Hierarchical clustering
1 overall cluster gathering sensors together 3 times out of 4
3

## Slide 13: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
Input data
Yearly average hydrograph
Complete timeseries of 5 years
1
Timeseries of monthly medians
Selection of the time period where most of the sensor are continuously recording – 5years
Subtraction of the period average level
Homogeneous dataset: 60sensors x 60months
Timeseries of monthly medians
Subtraction of the year average level
For each month: month mean
Homogeneous dataset: 79sensors x 12months

## Slide 14: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
Seasonal trends
Mann-Kendall test
Sen’s slope estimator
Timeseries of monthly medians
For each month: estimation of the seasonal trend slope?
Estimation of the overall trend slope
Homogeneous dataset: 79sensors x (12+1)
Timeseries of monthly medians
For each month: there is a statistically significant trend?
There is an overall significant trend?
Homogeneous dataset: 79sensors x (12+1)
Input data
1
Many sensors are recording an overall decreasing trend of the water table
 important to monitor the gw system

## Slide 15: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
PCA
Yearly average hydrograph
Complete timeseries of 5 years
2
PC1
PC2
PC1
PC2
Principal components
PCs meaning: 2 typical hydrograph
PC1: dry or wet years
PC2: kind of seasonality

## Slide 16: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
Yearly average hydrograph
Complete timeseries of 5 years
0
1
2
3
4
General agreement:
Only yearly hydrograph following used because it considers all dataset sensors
PCA
2
Previously identified clusters, in map

## Slide 17: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
Seasonal trends - Sen’s slope estimator
PC1
PC2
Clusters not as easily identifiable as before
3rd PC seems to be already noisy
PCA
2
PC1: general increasing trend
PC2: spring increasing trend
PC3: fall increasing trend

## Slide 18: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
Seasonal trends - Sen’s slope estimator
PC1
PC2
Not a clear trend or gathering
General negative PC1 in the central belt
PCA
2

## Slide 19: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
Hierarchical clustering
3
Multiple choices for applied methods:
How to define the distance to find the similarity between every pair of objects
How to link objects to group them into a binary, hierarchical cluster tree (distance between clusters)
Where to cut the hierarchical tree to split clusters
All methods combinations have been tried
Dissimilarity has been verified by comparing the cophenetic distances with the original distance data
Few combinations with highest cophenetic correlation coefficient are identified
For all input data type, one combination is always one of the best
The hierarchical tree has been cut basing on links relative consistency
Euclidean - Unweighted average has been selected

## Slide 20: Hierarchical clustering
EGU2020 - Online, 4-8 May 2020
Yearly av. hydrograph
Seasonal trends
PCA components
All previous variables
Hierarchical clustering
3
Overall cluster
grouping sensors in same clusters 3 times out of 4
13 clusters
35 not clustered sensors

## Slide 21: Methods comparison
EGU2020 - Online, 4-8 May 2020
13 clusters (44 sensors)
35 not clustered sensors
Complicated and longer
With multiple choices that affect results e.g. input data, clustering parameters
Possibly, more insights on the gw system thanks to Mann-Kendall, Sen’s slope and PCA
Hierarchical clustering (HC)
9 clusters (37 sensors)
42 not clustered sensors
Easy technique
Fast application
Not subjective choices
Oscillation correlation (OC)
Different sensors are grouped together
Area | OC | HC | Notes
Astico | 1 big cl + 1 | Mostly not clustered sensors | OC big cl: where there are paleochannels HC shows similar hydrographs but different trends and PCA components (slide 18)
Brenta – north | Different but comparable cl |  | OC cluster are correlated between themselves
Brenta – south | 2 small cl | 4 cl | OC clusters are maintained and enlarged in HC
Leogra- Timonchio | 1 cl | 2 cl | Few sensors, different couples OC cluster never together in HC
Vicenza | 1 small cl | 2 cl | The small OC cluster is recognized also in HC

## Slide 22: Oscillation correlation
Integral scale
Last
EGU2020 - Online, 4-8 May 2020
Microscale
Time interval in which hydraulic heads are perfectly correlated
5
80
days
Using the evaluated microscale as sampling time
For the dataset,
Percentage daily error ranges between 1.7 and 7.3%
with a mean error of 3.5%

## Slide 23: Optimization of existing Groundwater Level Monitoring Network Procedure
EGU2020 - Online, 4-8 May 2020
2- Other points: manually with longer sampling time
3- Sampling time defined with microscale
4- Extra sensors to uncovered areas
1- Only one sensor for each area
Correlation map
Hierarchical clusters
areas with similar behavior

## Slide 24
FOR FURTHER
QUESTIONS
mara.meggiorin@dicea.unipd.it
mmeggiorin@sinergeo.it
EGU2020 - Online, 4-8 May 2020
EGU General Assembly 2020, Online
Sharing Geoscience Online, 4-8 May, 2020