## Slide 1: Determination of trace elements and macronutrients in agricultural soils using energy dispersive X-ray fluorescence as a rapid and precise analytical technique
Maame Croffie 1, 2
(mcroffie01@qub.ac.uk)
Co-authors: Paul N. Williams 2, Owen Fenton 1, Anna Fenelon 1, Konrad Meztger 1, 3, Karen Daly 1
1Teagasc Agriculture and Food Development Authority, Crops Environment and Land Use Department
Wexford, Y35 TC97, Ireland
2 Institute for Global Food Security, Queen’s University Belfast, Northern Ireland, BT9 5DL, UK
3 International Network for Environment and Health, NUI Galway, H91 TK33, Ireland

## Slide 2
X-ray tube
Secondary target
sample
XRF
detector
XRF Spectra
Introduction
Advantages
Minimal sample preparation
Rapid
Inexpensive
Portable
Challenges
Particle size effects
Surface irregularity
Matrix effects
Moisture effects
Objective
Improve accuracy and precision for trace elements and macronutrient analysis

## Slide 3: Materials and Methods
Sample preparation
Loose powder
Calibration study
Fundamental parameters (FP)
Matching library (ML) made up of 4 CRMs
Pressed pellet + wax
vs
Pressed pellet
XRF analysis of ISE samples
Cu
Cr
Pb
Fe
Al
Ca
Ni
Mn
S
Mg
Zn
P
ISE-International Soil Exchange
(reference samples for proficiency testing of labs)

## Slide 4: Materials & Methods
Sampling sites
Energy-dispersive XRF
ICP-OES spectrometer
Aqua regia digestion
Pressed pellet with wax binder
Agreement statistics

## Slide 5: Results- Sample preparation comparison study

## Slide 6: Results-XRF calibration study
FP- fundamental parameters
ML- matching library

## Slide 7: Results- Comparison between XRF and ICP-OES
Ca
Zn
*Cu
Ni
Pb
Fe
Mn
Mg
S
P
Al
Cr
K
R 2 >0.80
CCC>0.90
R 2 >0.70
CCC<0.90>0.70
R 2 <0.70
CCC<0.70
CCC-concordance correlation coefficient
* bias corrected for to improve agreement

## Slide 8: Observed differences between XRF and ICP-OES by soil texture

## Slide 9: Conclusion
Pressed pellet with wax binder improves accuracy of XRF analysis
Matching library had varying effects on elements
XRF is more accurate for Al and K than aqua regia digestion with ICP-OES analysis
XRF can provide rapid determination of soil texture

## Slide 10: Acknowledgements
Linda Moloney Finn
Owen Frahill
Conor Nolan
Scott Rees